## Slide 1: Business Networking
  Managed Switch Comparison
1
Contents

## Slide 2
Vendor | TP-Link | UBNT | D-Link | MikroTik
Model | TL-SX3016F | US-16-XG | DXS-1100-16SC | CRS317-1G-16S+RM
Ports | 16* 10G SFP+ | 12* SFP+ + 4* 10GE | 14* SFP+ + 2* 10GE/SFP+ Combo | 1* GE + 16* 10G SFP+
SDN Support | √ | √ | × | ×
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | 1* RJ45
MAC Address Table | 32K | - | 16K | 32K
Packet Buffer | 3 MB | - | 2 MB | 3 MB
ACL | √ | √ | √ | √
QoS | √ | √ | √ | √
Multicast | √ | √ | √ | √
VLAN | √ | √ | √ | √
Static routing | 48 (IPv4, IPv6) | × | × | √
IP interfaces | 16 | × | × | √
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | × | √
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS* (Future upgrade) | × | × | √
Redundant power supply | √ | √ | × | √
Power Supply | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50-60 Hz 48/24 VDC | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50/60 Hz
Max. Power Consumption | 32.7 W | 36 W | 60 W | 44 W
FAN | 1 Fixd | 1 Fixed | 2 Fixed | 2 Flexible
Product comparison (10G Fiber Switch----TL-SX3016F)

## Slide 3
Vendor | TP-Link | UBNT | MikroTik
Model | TL-SX3008F | USW-Aggregation | CRS309-1G-8S+IN
Ports | 8* 10G SFP+ | 8* 10G SFP+ | 1* GE + 8* 10G SFP+
SDN Support | √ | √ | ×
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1*RB232
MAC Address Table | 32K | - | 32K
Packet Buffer | 2 MB | - | 2 MB
ACL | √ | √ | √
QoS | √ | √ | √
Multicast | √ | √ | √
VLAN Type | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | - | 802.1Q Tagged VLAN MAC VLAN Voice VLAN
Static routing | 48 (IPv4, IPv6) | × | √
IP interfaces | 16 | × | √
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | DHCP Server DHCP Snooping DHCP Relay
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS* (Future upgrade) | × | OAM/ DDM/ sFlow
Casing & Installation | Metal & Rackmount | Plastic & Desktop | Metal & Rackmount
Power Supply | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50/60 Hz | 802.3at PoE in; 12-57 VDC Adaptor
Max. Power Consumption | 15.5 W | 30 W | 23 W
Dimensions | 440 × 180 × 44 mm (rack) | 440 × 120 × 44 mm (rack) | 272 × 191 × 44 mm (rack)
Product comparison (10G Fiber Switch----TL-SX3008F)

## Slide 4
Vendor | TP-Link | UBNT | D-Link | NetGear | Trendnet
Model | TL-SG3210XHP-M2 | USW-Enterprise-8-PoE | DMS-1100-10TP | M4200-10MG-PoE+ | TPE-30102WS
Ports | 8* 2.5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+ | 6* 2.5G RJ45 + 2* 5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+
SDN Support | √ | √ | × | × | ×
Console Ports | 1* RJ45 + 1* Micro-USB | × | × | 1* RJ45 + 1* Micro-USB | 1* RJ45
MGMT Ports | × | × | × | 1 | ×
USB Ports | × | × | × | 1 | ×
PoE | 8 PoE+, 240 W | 8 PoE+, 120 W | 8 PoE+, 240 W | 8 PoE+, 240 W | 8 PoE+, 240 W
MAC Address Table | 16K | - | 16K | 16K | 32K
Packet Buffer | 12 Mbit | - | - | 16 Mbit | 16 Mbit
ACL | √ | √ | √ | √ | √
QoS | √ | √ | √ | √ | √
Multicast | √ | √ | √ | √ | √
VLAN Type | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | - | 802.1Q Tagged VLAN MAC VLAN Voice VLAN | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | 802.1Q Tagged VLAN Private VLAN Voice VLAN
Static routing | 48 (IPv4, IPv6) | * (Future upgrade) | × | 32 IPv4, 32 IPv6 | 32 (IPv4, IPv6)
RIP dynamic routing | × | × | × | 32 IPv4 | ×
IP interfaces | 16 | × | × | 64 | 8
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | × | DHCP Server DHCP Snooping DHCP Relay | DHCP Server DHCP Snooping DHCP Relay
TLS Version | 1.2 | - | 1.2 | 1.0 | 1.2
LAG Groups | 8 Groups | - | 8 Groups | 5 Groups | 4 Groups
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS* (Future upgrade) | × | ERPS | sFlow | ×
Casing & Installation | Metal & Rackmount | Plastic & Desktop | Metal & Rackmount | Metal & Rackmount | Metal & Rackmount
Product comparison (2.5G PoE Switch----TL-SG3210XHP-M2)

## Slide 5
Product comparison (24 SFP Switch with 10G Uplink----TL-SG3428XF)
Model | TP-Link TL-SG3428XF | D-Link DGS-1210-28XS/ME | MikroTik CRS328-4C-20S-4S+RM
Ports | 20 SFP + 4 SFP/RJ45 Combo + 4 SFP+ | 24 SFP + 4 SFP+ | 20 SFP + 4 SFP/RJ45 Combo + 4 SFP+
Console Ports | 1 RJ45 + 1 Micro-USB | 1 RJ45 | 1 RJ45
SDN support | √ | × | ×
MAC Address | 16K | 16K | 16K
Packet Buffer | 1.5MB | 1.5MB | 1.5MB
Flash | 32MB | 32MB | 16MB
RPS | √ | × | √
Fan | 1 | 1 | 2
VLAN Group | 4K | 4K | √
IP Interface | 16 | — | √
Static route | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | √
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | DHCP Server, DHCP Relay, DHCP Snooping | √
ISP Feature* | OAM, L2TP, DDM, sFlow | OAM, DDM, Dying Gasp | √
Advance Feature | × | × | √（RIP、OSPF、BGP）

## Slide 6
Product comparison (48 GE Switch with 10G Uplink----TL-SG3452X)
 | TP-Link TL-SG3452X | UBNT USW-Pro-48 | D-Link DGS-3000-52X | NetGear GC752X | Aruba 2540 48G 4SFP+ Switch
Port | 48 RJ45 + 4 SFP+ | 48 RJ45 + 4 SFP+ | 48 RJ45 + 4 SFP+ | 48 RJ45 + 2 SFP + 2 SFP+ | 48 RJ45 + 4 SFP+
Console | 1 RJ45 + 1 Micro-USB | × | 1 RJ45 | 1 Micro-USB | 1 RJ45 + 1 Micro-USB
SDN support | √ | √ | × | √ | √
MAC Address | 16K | √ | 16K | 16K | 16K
VLAN Group | 4K | √ | 4K | 256 | 512
IP Interface | 16 | √ | 16 | 15 | -
Static route | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | 256 (IPv4, IPv6)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | DHCP Server | DHCP Server, DHCP Relay, DHCP Snooping | DHCP snooping | DHCP Server, DHCP Relay
ISP Feature* | OAM, L2TP, DDM, sFlow | × | OAM, L2TP, sFlow, Dying Gasp, CFM, Y.1731 OAM | × | sFlow
USB | × | × | × | 1 | ×
RPS | × | √ | √ | × | ×
PoE budget | 32.7W | 60W | 40.7W | 43.9W | 46.6W
Fan | None | None | 2 | 1 | 1

## Slide 7
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3428XMP | USW-Pro-24-PoE | DGS-3000-28XMP | GC728XP | MS125-24P-HW | 2540 24G PoE+ 4SFP+ Switch
Ports | 24* GE + 4* 10G SFP+ | 24* GE + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 2* SFP + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 4* 10G SFP+
SDN Support | √ | √ | × | √ | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 24 PoE+, 384 W | 16 PoE+, 8 PoE++, 400 W | 24 PoE+, 370 W | 24 PoE+, 390 W | 24 PoE+, 370 W | 24 PoE+, 370 W
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 36 Mbit Ingress 62.2 Mbit Egress
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | - | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
AAA | √ | - | √ | √ | √ | √
IP interfaces | 16 | - | 16 | 15 | × | -
Static routing | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | × | 256 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Server | DHCP Server DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay | DCHP Server DHCP Relay
ISP Feature | OAM/ L2TP/ DDM/ sFlow ERPS* (Future upgrade) | × | OAM/ L2TP/ sFlow | × | × | sFlow
Product comparison (24 GE PoE Switch with 10G Uplink----TL-SG3428XMP)

## Slide 8
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3428X | USW-Pro-24 | DGS-3000-28X | GC728X | MS125-24-HW | 2540 24G 4SFP+ Switch
Ports | 24* GE + 4* 10G SFP+ | 24* GE + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 2* SFP + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 4* 10G SFP+
SDN Support | √ | √ | × | √ | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
MAC Address Table | 16K | - | - | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 36 Mbit Ingress 62.2 Mbit Egress
ACL | √ | √ | √ | √ | √ | √
QoS | √ | √ | - | √ | √ | √
LAG | √ | √ | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | - | √ | √ | √ | √
802.1x | √ | - | √ | √ | √ | √
STP | √ | - | √ | √ | √ | √
AAA | √ | - | √ | √ | √ | √
IP interfaces | 16 | - | 16 | 15 | × | -
Static routing | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | × | 256 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Server DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay | DCHP Server DHCP Relay
ISP Feature | OAM/ L2TP/ DDM/ sFlow ERPS* (Future upgrade) | - | OAM/ L2TP/ sFlow | × | × | sFlow
Product comparison (24 GE Switch with 10G Uplink----TL-SG3428X)

## Slide 9
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3452P v1/v2 | USW-48-PoE | DGS-1210-52MP/ME | GS752TPv2 | MS120-48LP-HW | 2530-48G-PoE+ Switch
Ports | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 50* GE + 2* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | × | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 48 PoE+, 384W | 32 PoE+, 195W | 40 PoE, 8 PoE+, 370W | 48 PoE+, 380W | 48 PoE+, 370W | 48 PoE+, 382W
MAC Address Table | 16K | - | 16K | 16K | 32K | 16K
Packet Buffer | 12 Mbit | - | 24 Mbit | 12 Mbit | - | 24 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 16 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 15 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 32 IPv4, 32 IPv6 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | × | × | OAM, DDM, Dying Gasp, ERPS | × | × | sFlow
Product comparison (48 GE PoE Switch----TL-SG3452P)

## Slide 10
Vendor | TP-Link | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3452 | DGS-1210-52/ME | GS748Tv5 | MS120-48-HW | 2530-48G Switch
Ports | 48* GE + 4* SFP | 48* GE + 4* SFP | 46* GE + 2 GE/SFP Combo + 2* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP
SDN Support | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | × | 1* RJ45 + 1* Micro-USB
RPS | × | √ | × | × | ×
MAC Address Table | 16K | 16K | 16K | 32K | 16K
Packet Buffer | 12 Mbit | 24 Mbit | 12 Mbit | - | 24 Mbit
ACL | √ | √ | √ | √ | √
QoS | √ | √ | √ | √ | √
VLAN Group | 4K | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √
AAA | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 16 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | × | 15 | × | ×
Static routing | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | 32 IPv4, 32 IPv6 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | × | OAM, DDM, Dying Gasp, ERPS | × | × | sFlow
Product comparison (48 GE Switch----TL-SG3452)

## Slide 11
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3428MP v2/v3 | US-24-500W | DGS-1210-28MP/ME | M4100-26G-PoE | MS120-24P-HW | 2530-24G-PoE+ Switch
Ports | 24* GE + 4* SFP | 24* GE + 2* SFP | 24* GE + 4* SFP | 24* GE + 2* GE/SFP Combo + 2* SFP | 24* GE + 4* SFP | 26* GE + 2* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | 1* RJ45 | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 24 PoE+, 384W | 24 PoE+, 470W | 24 PoE+, 370W | 24 PoE+, 380W | 24 PoE+, 370W | 24 PoE+, 195W
RPS | × | × | × | √ | × | ×
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 12 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 1K | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 12 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 64 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 64 IPv4 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM, sFlow ERPS* (Future upgrade) | × | OAM, DDM, Dying Gasp, ERPS | sFlow | × | sFlow
Product comparison (24 GE PoE Switch----TL-SG3428MP)

## Slide 12
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | TL-SG3428 v2 | US-24 | DGS-1210-28/ME | M4100-26G | MS120-24-HW | 2530-24G Switch
Ports | 24* GE + 4* SFP | 24* GE + 2* SFP | 24* GE + 4* SFP | 24* GE + 2* GE/SFP Combo + 2* SFP | 24* GE + 4* SFP | 24* GE + 4* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | 1* RJ45 | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
RPS | × | × | √ | √ | × | ×
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 12 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 1K | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 12 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 64 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 64 IPv4 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM, sFlow ERPS* (Future upgrade) | × | OAM, DDM, Dying Gasp, ERPS | sFlow | × | sFlow
Product comparison (24 GE Switch----TL-SG3428)

## Slide 13
Vendor | TP-Link | D-Link | NetGear | Aruba
Model | TL-SG3210 v3 | DGS-1210-10/ME | GC110 | 2530-8G Switch
Ports | 8* GE + 2* SFP |  |  | 
SDN Support | √ | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | 1* RJ45 + 1* Micro-USB
RPS | × | √ | × | ×
MAC Address Table | 8K | 16K | 16K | 16K
Packet Buffer | 4.1 Mbit | 12 Mbit | 12 Mbit | 12 Mbit
ACL | √ | √ | √ | √
QoS | √ | √ | √ | √
VLAN Group | 4K | 4K | 1K | 512
Multicast Group | 511 | 256 | 512 | -
ARP | 316 | 256 | 384 | -
802.1x | √ | √ | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 5 Groups | 8 Groups
IP interfaces | 16 | × | 15 | ×
Static routing | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | 64 IPv4 | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM | OAM, DDM, Dying Gasp, ERPS | × | sFlow
Installation | Desktop, Rackmount | Desktop, Rackmount | Desktop, Wall-mount | Desktop, Rackmount
Product comparison (8 GE Switch----TL-SG3210)

## Slide 14
Vendor | TP-Link | D-Link | NetGear | Cisco
Model | TL-SG2428P v1/v2 | DBS-2000-28P | GS728TP | CBS250-24P-4G
Ports | 24* GE + 4* SFP | 24* GE + 4* GE/SFP Combo | 24* GE + 4* SFP | 24* GE + 4* SFP
SDN Support | √ | √ | × | ×
Console Ports | × | 1* RJ45 | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1
PoE | 24 PoE+, 250W | 24 PoE+, 193W | 16 PoE, 8 PoE+, 192W | 24 PoE+, 195W
MAC Address Table | 8K | 8K | 8K | 8K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 8 Mbit | 8 Mbit
ACL | √ | √ | √ | √
QoS | √ | × | √ | √
VLAN Group | 4K | 256 | 256 | 255
Multicast | √ | √ | √ | √
802.1x | √ | × | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 8 Groups | 4 Groups
IP interfaces | 16 | × | 32 | 16
Static routing | 32 (IPv4, IPv6) | × | 32 IPv4 | 32 IPv4
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | DHCP Snooping | DHCP Relay
Product comparison (24 GE PoE Smart Switch----TL-SG2428P)

## Slide 15
Vendor | TP-Link TL-SG2218P | UBNT USW-16-PoE | NetGear GS716TP | Cisco CBS250-16P-2G
Ports | 16* Gigabit RJ45 Ports + 2* Gigabit SFP Slots |  |  | 
PoE ports | 16* PoE+, max 30W/port | 8* PoE+, max 30W/port | 16* PoE, max 30W/port | 16* PoE, max 30W/port
PoE budget | 150W | 42W | 180W | 120W
Packet Buffer | 4.1 Mbit | - | 12 Mbit | 12 Mbit
MAC Address | 8K | - | 16K | 8K
VLAN Group | 4K | - | 256 | 255
SDN Support | √ | √ | √ | ×
IP Interface | 16 | × | × | 16
Static route | 32 (IPv4, IPv6) | × | × | 32 (IPv4, IPv6)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | × | DHCP Snooping | DHCP Relay
Dimensions | 17.3 × 7.1 × 1.7 in (440 × 180 × 44 mm) | 17.4 × 7.9 × 1.7 in (442 × 200 × 44 mm) | 17.3 × 8.0 × 1.7 in (440 × 204 × 43 mm) | 10.6 × 11.7 × 1.7 in (268 × 297 × 44 mm)
Fan | 1 | Fanless | 1 | Fanless
Product comparison (16 GE PoE Smart Switch----TL-SG2218P)

## Slide 16
Vendor | TP-Link | D-Link | NetGear | Aruba
Model | TL-SG2218 | DGS-1210-20 | GS716Tv3 | 1920 16G Switch
Ports | 16* GE + 2* SFP | 16* GE + 4* SFP | 16* GE + 2* SFP | 16* GE + 4* SFP
SDN Support | √ | × | × | ×
Console Ports | × | × | × | 1* RJ45
MAC Address Table | 8K | 8K | 16K | 8K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 2 Mbit | 4.1 Mbit
ACL | 230 | 200 | 100 | -
ARP | 316 | 128 | 512 | -
QoS | √ | × | √ | √
VLAN Group | 4K | 256 | 256 | 4K
Multicast | √ | √ | √ | √
802.1x | √ | × | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 26 Groups | 8 Groups
IP interfaces | 16 | × | 15 | 8
Static routing | 32 (IPv4, IPv6) | × | 32 IPv4 | 32 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Snooping | DHCP Snooping | DHCP Relay
Product comparison (16 GE Smart Switch----TL-SG2218)

## Slide 17
Vendor | TP-Link TL-SG2016P | UBNT USW-Lite-16-PoE | NetGear GS516TP
Ports | 16* Gigabit RJ45 | 16* Gigabit RJ45 | 16* Gigabit RJ45
PoE ports | 8* PoE+, max 30W/port | 8* PoE+, max 30W/port | 8* PoE, max 15.4W/port
PoE budget | 120W | 45W | 76W
MAC Address | 8K | - | 8K
VLAN Group | 4K | - | 256
SDN Support | √ | √ | ×
IP Interface | 16 | × | √
Static route | 32 (IPv4, IPv6) | × | 32 (IPv4)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | × | DHCP Snooping
Dimensions | 286*111.7*25.4 mm | 191.7*185*43.7 mm | 328*169*43 mm
Fan | × | × | √
Power Supply | 53.5VDC/2.43A | 100-240V AC | 100-240V AC
Mounting | Desktop/ Wall-mount | Desktop | Rackmount
Product comparison (16 GE Smart PoE Switch----TL-SG2016P)

## Slide 18
Vendor | TP-Link | UBNT | D-Link | NetGear | Aruba | Meraki
Model | TL-SG2210MP v1/v2 | US-8-150W | DBS-2000-10MP | GS510TP | 1920 8G PoE+ (150W) switch | MS120-8FP-HW
Ports | 8* GE + 2* SFP |  |  |  |  | 
SDN Support | √ | √ | √ | × | × | √
Console Ports | × | × | × | × | 1* RJ45 | ×
PoE | 8 PoE+, 150W | 8 PoE+, 130W | 8 PoE+, 130W | 8 PoE+, 130W | 8 PoE+, 180W | 8 PoE+, 124W
Fan | 1 | × | × | 1 | 1 | ×
MAC Address Table | 8K | 16K | 8K | 4K | 8K | 16K
Packet Buffer | 4.1 Mbit | - | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | -
QoS | √ | - | × | √ | √ | √
VLAN Group | 4K | 255 | 256 | 64 | 4K | 4K
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | × | √ | √ | √
STP | √ | - | √ | √ | √ | √
LAG Groups | 8 Groups | 6 Groups | - | - | 4 Groups | -
IP interfaces | 16 | × | × | × | 8 | ×
Static routing | 32 (IPv4, IPv6) | × | × | × | 32 (IPv4, IPv6) | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | × | DHCP Relay | DHCP Relay DHCP Snooping
Installation | Desktop, Rackmount | Desktop | Desktop, Rackmount | Desktop, Rackmount | Desktop, Rackmount | Desktop, Wall-mount
Product comparison (8 GE Smart PoE Switch----TL-SG2210MP)

## Slide 19
Vendor | TP-Link | D-Link | NetGear | Aruba | Meraki
Model | TL-SG2210P v3.2/v4 | DGS-1210-10P | GS110TPv3 | 1920 8G PoE+ (65W) switch | MS120-8FP-HW
Ports | 8* GE + 2* SFP |  |  |  | 
SDN Support | √ | × | × | × | √
Console Ports | × | × | × | 1* RJ45 | ×
PoE | 8 PoE+, 61W | 8 PoE+, 65W | 8 PoE, 46W | 8 PoE+, 65W | 8 PoE+, 67W
Fan | × | × | 1 | × | ×
MAC Address Table | 8K | 8K | 4K | 8K | 16K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | -
QoS | √ | × | √ | √ | √
VLAN Group | 4K | 256 | 64 | 4K | 4K
Multicast | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √
LAG Groups | 8 Groups | 4 Groups | - | 4 Groups | -
IP interfaces | 16 | × | × | 8 | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 (IPv4, IPv6) | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | DHCP Relay | DHCP Relay DHCP Snooping
Installation | Desktop, Wall-mount | Desktop, Rackmount | Desktop, Wall-mount | Desktop, Rackmount | Desktop, Wall-mount
Product comparison (8 GE Smart PoE Switch----TL-SG2210P)

## Slide 20
Vendor | TP-Link | UBNT |  | HPE
Model | TL-SG2008P v1/v2 | USW-Lite-8-PoE | US-8-60W | 1920S 8G PPoE+ 65W Switch
Ports | 8* GE |  |  | 
SDN Support | √ |  |  | ×
PoE | 4 PoE+, 62W | 4 PoE+, 52W | 4 PoE, 48W | 4 PoE+, 65W
PoE Standard | 802.3af/at | 802.3af/at | 802.3af | 802.3af/at
Fan | × |  |  | 
MAC Address Table | 8K | - | - | 8K
Packet Buffer | 4.1 Mbit | - | - | 12 Mbit
QoS | √ | - | - | √
VLAN Group | 4K | - | - | 4K
Multicast | √ | - | - | √
802.1x | √ | √ | √ | √
STP | √ | - | - | √
LAG Groups | 8 Groups | - | - | 4 Groups
IP interfaces | 16 | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 IPv4
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | DHCP Relay
Installation | Desktop, Wall-mount |  |  | Rackmount
Shell material | Metal | Plastic | Metal | Metal
Product comparison (8 GE Smart PoE Switch----TL-SG2008P)

## Slide 21
Vendor | TP-Link | UBNT | Meraki | NetGear | Aruba | D-Link
Model | TL-SG2008 v3/v4 | US-8 | MS120-8-HW | GS108Tv3 | 1920S 8G Switch | DGS-1210-10
Ports | 8* GE | 8* GE | 8* GE + 2* SFP | 8* GE | 8* GE | 8* GE + 2* SFP
SDN Support | √ | √ | √ | √ | × | ×
MAC Address Table | 8K | - | 16K | 8K | 8K | 8K
Packet Buffer | 4.1 Mbit | - | - | 4.1 Mbit | 12 Mbit | 4.1 Mbit
QoS | √ | - | √ | √ | √ | ×
VLAN Group | 4K | - | 4K | 64 | 4K | 256
Multicast | √ | - | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | - | √ | √ | √ | √
LAG Groups | 8 Groups | - | - | 8 Groups | 4 Groups | 4 Groups
IP interfaces | 16 | × | × | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 IPv4 | 32 IPv4 | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Relay | ×
Power Supply | 12 V/1 A DC PoE in | 48 V/0.5 A DC PoE in | 54 V/1.67 A DC | 12 V/1 A DC PoE in | 100-240 V AC ~ 50/60 Hz | 100-240 V AC ~ 50/60 Hz
PoE Passthrough | × | √ (12W) | × | × | × | ×
Installation | Desktop, Wall-mount | Desktop, Wall-mount | Desktop, Wall-mount | Desktop, Rackmount | Rackmount | Desktop, Rackmount
Product comparison (8 GE Smart Switch----TL-SG2008)

## Slide 22
Product comparison (8 GE Smart PoE Switch)
Vendor | TP-Link |  | 
Model | TL-SG2008P v1/v2 | TL-SG2210P v3.2/v4 | TL-SG2210MP v1/v2
Ports | 8* GE | 8* GE + 2* SFP | 
SDN Support | √ |  | 
PoE | 4 PoE+, 62W | 8 PoE+, 61W | 8 PoE+, 150W
Average PoE power / port | 15.5W | 7.6W | 18.7W
IP interfaces | 16 |  | 
Static routing | 32 (IPv4, IPv6) |  | 
DHCP | DHCP Server DHCP Relay DHCP Snooping |  | 
Installation | Desktop, Wall-mount |  | Desktop, Rackmount
FAN | × |  | 1
Features | The average PoE power of a single port is 15.5W, which is higher than 11ac EAP, that is, 4 PoE ports can be connected to 11ac EAP at the same time; 4 non-PoE ports can be used to connect wired devices; Desktop fanless design, flexible deployment, can be used in home, office and other scenarios; | 8 PoE ports, the average PoE power of a single port is 7.6W, which can be fully loaded with 11ac panel APs; The optical port can meet the needs of long-distance transmission; Desktop fanless design, flexible deployment, can be used in home, office and other scenarios; | 8 PoE ports, the average PoE power of a single port is 18.7W, which can be fully loaded with 11ac EAP; The optical port can meet the needs of long-distance transmission; Rack-type design, which can meet the rack installation scenarios of small and medium-sized enterprises;
Vendor | TP-Link |  | 
Model | TL-SG2008P v1/v2 | TL-SG2210P v3.2/v4 | TL-SG2210MP v1/v2
Ports | 8* GE | 8* GE + 2* SFP | 
SDN Support | √ |  | 
PoE | 4 PoE+, 62W | 8 PoE+, 61W | 8 PoE+, 150W
Average PoE power / port |  |  | 
IP interfaces | 16 |  | 
Static routing | 32 (IPv4, IPv6) |  | 
DHCP | DHCP Server DHCP Relay DHCP Snooping |  | 
Installation | Desktop, Wall-mount |  | Desktop, Rackmount
FAN | × |  | 1
Features | The average PoE power of a single port is 15.5W, which is higher than 11ac EAP, that is, 4 PoE ports can be connected to 11ac EAP at the same time; 4 non-PoE ports can be used to connect wired devices; Desktop fanless design, flexible deployment, can be used in home, office and other scenarios; | 8 PoE ports, the average PoE power of a single port is 7.6W, which can be fully loaded with 11ac panel APs; The optical port can meet the needs of long-distance transmission; Desktop fanless design, flexible deployment, can be used in home, office and other scenarios; | 8 PoE ports, the average PoE power of a single port is 18.7W, which can be fully loaded with 11ac EAP; The optical port can meet the needs of long-distance transmission; Rack-type design, which can meet the rack installation scenarios of small and medium-sized enterprises;

## Slide 23
Vendor | TP-Link | NetGear | D-Link | Trendnet
Model | TL-SL2428P v4.2 | FS728TP | DES-1210-28P | TPE-224WS (C1.0R)
Ports | 24* FE + 2* GE + 2* GE/SFP Combo |  |  | 
SDN Support | √ | × | × | ×
PoE | 24 PoE+, 250W | 24 PoE, 192W | 20 PoE, 4 PoE+, 193W | 20 PoE, 4 PoE+, 193W
MAC Address Table | 8K | 4K | 8K | 8K
Packet Buffer | 4.1 Mbit | 8 Mbit | 4.1 Mbit | 4.1 Mbit
QoS | √ | √ | √ | √
VLAN Group | 4K | 128 | 256 | 256
Multicast | √ | √ | √ | √
802.1x | √ | √ | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 8 Groups | -
IPv6 | √ | × | √ | √
IP interfaces | 16 | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | ×
IPv6 | √ | × | √ | √
Fan | 2 | 1 | 3 | 2
Product comparison (24 FE Smart Switch----TL-SL2428P)