## Slide 1: Switch 竞品对比

## Slide 2
Vendor & Model | TP-Link SG6654XHP | D-Link DGS-3130-54PS | Cisco CBS350-48FP-4X | NetGear M5300-52G-POE+ | Ruijie Reyee RGNBS5200- 48GT4XSUP | Aruba Instant On 1960 48G 40p Class4 8p Class6 PoE 2XGT 2SFP+ 600W Switch | RUCKUS ICX7150-48P
Ports | 48* GE RJ45 6* 10G SFP+ | 48* GE RJ45 2* 10G RJ45 4* 10G SFP+ | 48* GE RJ45 4* 10G SFP+ | 44* GE RJ45, 4* GE RJ45/SFP Combo 2* 10G RJ45/SFP+ Combo 1 expansion slot (max 2* 10G SFP+） | 48* GE RJ45 4* 10G SFP+ | 48* GE RJ45 2* 10G RJ45 2* 10G SFP+ | 50* GE RJ45 4* 10G SFP+
PoE | 48* GE PoE+, max PoE Budget 1440W, by default is 764W | 48* GE PoE+, max PoE Budget 740W, by default is 370W | 48* GE PoE+, max and default PoE Budget is 740W | 48* GE PoE+, max PoE Budget 1440W, by default is 380W | 40* GE PoE+, 8* GE PoE++, max and default PoE Budget is 740W | 40* GE PoE+ & 8* GE PoE++, max and default PoE Budget is 600W | 48* GE PoE+, max and default PoE Budget is 370W
Console Port | 1* RJ45 + 1* USB Type-C | 1* RJ45 | 1* RJ45 | 1* RS232 + 2* Mini-USB | × | × | 1* RJ45 + 1* USB Type-C
Management Port | 1* RJ45 | 1* RJ45 | × | × | × | × | 1* RJ45
USB Ports | 2* USB2.0 | 1* USB2.0 | 1* USB2.0 | 1* USB2.0 | × | × | 1* USB2.0
Packet Buffer Memory | 3 MB | 4 MB | 3 MB | 4 MB | 2 MB | 1.5 MB | 4 MB
MAC Address | 32K | 16K | 16K | 32K | 16K | 16K | 16K
Flash | 8 MB Nor + 8 GB EMMC | N/A | 256 MB | 128 MB | 256 MB | 512MB NAND | 2 GB
DRAM | 4 GB DDR4 | N/A | 512 MB | 512 MB | - | 1GB DDR3 | 1 GB
CPU | Dual-core @1.5GHz | N/A | 800 MHz | 800 MHz | - | Single-Core @800MHz | -
Redundant Power Supply | 2 hot swappable power supply module, shipping with a PSM900-AC | Need external PSU | × | Need external PSU | × | × | ×
FAN | 4 hot swappable fan modules, N+1 redundant | 4 fixed Fans | 1 fixed Fans | Fixed Fan | 3 fixed Fans | Fixed Fans | Fixed Fans
Stacking Ports | 6 (the uplink ports can also use as stacking ports) | 4 | 4 | 4 (the uplink ports can also use as stacking ports) | × | 4 | 4 (the uplink ports can also use as stacking ports)
Stacking Number | 4 units per stack (Will support to 8 by FW upgrade at end of 24.Q1) | 6 units per stack | 4 units per stack | 8 units per stack | × | 4 units per stack | 12 units per stack
Entries | 2K IGMP groups | 1K IGMP groups | - | 2K IGMP groups | N/A | N/A | N/A
 | 64 groups LAG | 32 groups LAG | 8 groups LAG | 64 groups LAG | 16 groups LAG | N/A | N/A
 | 1K static IGMP groups | 128 static IGMP groups | - | N/A | N/A | N/A | N/A
 | 4K MLD Groups | 1K MLD Groups | - | N/A | N/A | N/A | N/A
 | 8K ARP Entries | 2K ARP Entries | - | 6K ARP Entries | N/A | N/A | 4K ARP Entries
 | 256 IP interfaces | 16 IP interfaces | 128 IP interfaces | 128 IP interfaces | N/A | N/A | N/A
 | 8K IPv6 ND Entries | 1K IPv6 ND Entries | - | N/A | N/A | N/A | N/A
 | 16K hardware routing | 3K hardware routing | - | 12K hardware routing | N/A | N/A | 6K hardware routing
 | 1024 Static Route | 512 Static Route | 990 static routes | 1024 Static Route | N/A | 32 Static Route | N/A
L3 Routing | Static Route, RIP, OSPF, ECMP | Static Route, PBR, RIP, OSPF, ECMP | Static Route, PBR, RIP | Static Route, RIP, OSPF, ECMP | Static Route, RIP, OSPF | Static Route | Static Route, RIP, ECMP (OSPF, PBR with license)
VRRP | √ | √ | × | √ | × | × | √ (with license)
Multicast Routing | PIM-DM (Will support PIM-SM by FW upgrade at end of 24.Q1) | PIM-SM | × | PIM-SM, PIM-DM | × | × | PIM-SM, PIM-SSM, PIM-DM (with license)
ERPS | √ | √ | × | × | × | × | ×
Product comparison (48 port L3 PoE Switch---- SG6654XHP)

## Slide 3
Vendor & Model | TP-Link SG6428XHP | D-Link DGS-3130-30PS | Cisco CBS350-24FP-4X | NetGear M5300-28G-POE+ | Ruijie Reyee RGNBS5200- 24GT4XS-P | Aruba Instant On 1960 24G 20p Class4 4p Class6 PoE 2XGT 2SFP+ 370W Switch | RUCKUS ICX 7150-24P
Ports | 24* GE RJ45 4* 10G SFP+ | 24* GE RJ45 2* 10G RJ45 4* 10G SFP+ | 24* GE RJ45 4* 10G SFP+ | 20* GE RJ45, 4* GE RJ45/SFP Combo 2* 10G RJ45/SFP+ Combo 1 expansion slot (max 2* 10G SFP+） | 24* GE RJ45 4* 10G SFP+ | 24* GE RJ45 2* 10G RJ45 2* 10G SFP+ | 26* GE RJ45 4* 10G SFP+
PoE | 24* GE PoE+, max PoE Budget 720W, by default is 402W | 24* GE PoE+, max PoE Budget 720W, by default is 370W | 24* GE PoE+, max and default PoE Budget is 370W | 24* GE PoE+, max PoE Budget 720W, by default is 380W | 24* GE PoE+, max and default PoE Budget is 370W | 20* GE PoE+ & 4* GE PoE++, max and default PoE Budget is 370W | 12* GE PoE & 12* GE PoE+, max and default PoE Budget is 370W
Console Port | 1* RJ45 + 1* USB Type-C | 1* RJ45 | 1* RJ45 | 1* RS232 + 1* Mini-USB | × | × | 1* RJ45 + 1* USB Type-C
Management Port | 1* RJ45 | 1* RJ45 | × | × | × | × | 1* RJ45
USB Ports | 2* USB2.0 | 1* USB2.0 | 1* USB2.0 | 1* USB2.0 | × | × | 1* USB2.0
Packet Buffer Memory | 3 MB | 2 MB | 1.5 MB | 2 MB | 1.5 MB | 1.5 MB | 2 MB
MAC Address | 32K | 16K | 16K | 32K | 16K | 16K | 16K
Flash | 8 MB Nor + 8 GB EMMC | N/A | 256 MB | 128 MB | 256 MB | 512MB NAND | 2 GB
DRAM | 4 GB DDR4 | N/A | 512 MB | 512 MB | N/A | 1GB DDR3 | 1 GB
CPU | Dual-core @1.5GHz | N/A | 800 MHz | 800 MHz | N/A | Single-Core @800MHz | N/A
Redundant Power Supply | 2 hot swappable power supply module, shipping with a PSM500-AC | Need external PSU | × | Need external PSU | × | × | ×
FAN | 4 hot swappable fan modules, N+1 redundant | 3 fixed Fans | 1 fixed Fans | Fixed Fan | 2 fixed Fans | Fixed Fans | 2 fixed Fans
Stacking Ports | 4 (the uplink ports can also use as stacking ports) | 4 | 4 | 4 (the uplink ports can also use as stacking ports) | × | 4 | 4 (the uplink ports can also use as stacking ports)
Stacking Number | 4 units per stack (Will support to 8 by FW upgrade at end of 24.Q1) | 9 units per stack | 4 units per stack | 8 units per stack | × | 4 units per stack | 12 units per stack
Entries | 2K IGMP groups | 1K IGMP groups | N/A | 2K IGMP groups | N/A | N/A | N/A
 | 64 groups LAG | 32 groups LAG | 8 groups LAG | 64 groups LAG | 16 groups LAG | N/A | N/A
 | 1K static IGMP groups | 128 static IGMP groups | N/A | N/A | N/A | N/A | N/A
 | 4K MLD Groups | 1K MLD Groups | N/A | N/A | N/A | N/A | N/A
 | 8K ARP Entries | 2K ARP Entries | N/A | 6K ARP Entries | N/A | N/A | 4K ARP Entries
 | 256 IP interfaces | 16 IP interfaces | 128 IP interfaces | 128 IP interfaces | N/A | N/A | N/A
 | 8K IPv6 ND Entries | 1K IPv6 ND Entries | N/A | N/A | N/A | N/A | N/A
 | 16K hardware routing | 3K hardware routing | N/A | 12K hardware routing | N/A | N/A | 6K hardware routing
 | 1024 Static Route | 512 Static Route | 990 static routes | 1024 Static Route | N/A | 32 Static Route | N/A
L3 Routing | Static Route, RIP, OSPF, ECMP | Static Route, PBR, RIP, OSPF, ECMP | Static Route, PBR, RIP | Static Route, RIP, OSPF, ECMP | Static Route, RIP, OSPF | Static Route | Static Route, RIP, ECMP (OSPF, PBR with license)
VRRP | √ | √ | × | √ | × | × | √ (with license)
Multicast Routing | PIM-DM (Will support PIM-SM by FW upgrade at end of 24.Q1) | PIM-SM | × | PIM-SM, PIM-DM | × | × | PIM-SM, PIM-SSM, PIM-DM (with license)
ERPS | √ | √ | × | × | × | × | ×
Product comparison (24 port L3 PoE Switch---- SG6428XHP)

## Slide 4
Product comparison (24 port L3 Non-PoE Switch---- SG6428X)
Vendor & Model | TP-Link SG6428X | D-Link DGS-3130-30TS | Cisco CBS350-24T-4X | NetGear M5300-28G | Ruijie Reyee RGNBS5200-24GT4XS | Aruba Instant On 1960 24G 2XGT 2SFP+ Switch | RUCKUS ICX 7150-24
Ports | 24* GE RJ45 4* 10G SFP+ | 24* GE RJ45 2* 10G RJ45 4* 10G SFP+ | 24* GE RJ45 4* 10G SFP+ | 20* GE RJ45, 4* GE RJ45/SFP Combo 2* 10G RJ45/SFP+ Combo 1 expansion slot (max 2* 10G SFP+） | 24* GE RJ45 4* 10G SFP+ | 24* GE RJ45 2* 10G RJ45 2* 10G SFP+ | 26* GE RJ45 4* 10G SFP+
Console Port | 1* RJ45 + 1* USB Type-C | 1* RJ45 | 1* RJ45 | 1* RS232 + 1* Mini-USB | × | × | 1* RJ45 + 1* USB Type-C
Management Port | 1* RJ45 | 1* RJ45 | × | × | × | × | 1* RJ45
USB Ports | 2* USB2.0 | 1* USB2.0 | 1* USB2.0 | 1* USB2.0 | × | × | 1* USB2.0
Packet Buffer Memory | 3 MB | 2 MB | 1.5 MB | 2 MB | 1.5 MB | 1.5 MB | 2 MB
MAC Address | 32K | 16K | 16K | 32K | 16K | 16K | 16K
Flash | 8 MB Nor + 8 GB EMMC | N/A | 256 MB | 128 MB | 256 MB | 512MB NAND | 2 GB
DRAM | 4 GB DDR4 | N/A | 512 MB | 512 MB | N/A | 1GB DDR3 | 1 GB
CPU | Dual-core @1.5GHz | N/A | 800 MHz | 800 MHz | N/A | Single-Core @800MHz | N/A
Redundant Power Supply | 2 fixed Power Supply module | Need external PSU | × | Need external PSU | × | × | ×
FAN | 4 fixed Fans | 2 fixed Fans | Fanless | Fixed Fan | 1 fixed Fan | Fanless | Fanless
Stacking Ports | 4 (the uplink ports can also use as stacking ports) | 4 | 4 | 4 (the uplink ports can also use as stacking ports) | × | 4 | 4 (the uplink ports can also use as stacking ports)
Stacking Number | 4 units per stack (Will support to 8 by FW upgrade at end of 24.Q1) | 9 units per stack | 4 units per stack | 8 units per stack | × | 4 units per stack | 12 units per stack
Entries | 2K IGMP groups | 1K IGMP groups | N/A | 2K IGMP groups | N/A | N/A | N/A
 | 64 groups LAG | 32 groups LAG | 8 groups LAG | 64 groups LAG | 16 groups LAG | N/A | N/A
 | 1K static IGMP groups | 128 static IGMP groups | N/A | N/A | N/A | N/A | N/A
 | 4K MLD Groups | 1K MLD Groups | N/A | N/A | N/A | N/A | N/A
 | 8K ARP Entries | 2K ARP Entries | N/A | 6K ARP Entries | N/A | N/A | 4K ARP Entries
 | 256 IP interfaces | 16 IP interfaces | 128 IP interfaces | 128 IP interfaces | N/A | N/A | N/A
 | 8K IPv6 ND Entries | 1K IPv6 ND Entries | N/A | N/A | N/A | N/A | N/A
 | 16K hardware routing | 3K hardware routing | N/A | 12K hardware routing | N/A | N/A | 6K hardware routing
 | 1024 Static Route | 512 Static Route | 990 static routes | 1024 Static Route | N/A | 32 Static Route | N/A
L3 Routing | Static Route, RIP, OSPF, ECMP | Static Route, PBR, RIP, OSPF, ECMP | Static Route, PBR, RIP | Static Route, RIP, OSPF, ECMP | Static Route, RIP, OSPF | Static Route | Static Route, RIP, ECMP (OSPF, PBR with license)
VRRP | √ | √ | × | √ | × | × | √ (with license)
Multicast Routing | PIM-DM (Will support PIM-SM by FW upgrade at end of 24.Q1) | PIM-SM | × | PIM-SM, PIM-DM | × | × | PIM-SM, PIM-SSM, PIM-DM (with license)
ERPS | √ | √ | × | × | × | × | ×

## Slide 5
Product comparison (48 port L3 Non-PoE Switch---- SG6654X)
Vendor & Model | TP-Link SG6654X | D-Link DGS-3130-54TS | Cisco CBS350-48T-4X | NetGear M5300-52G | Ruijie Reyee RGNBS5200- 48GT4XS | Aruba Instant On 1960 48G 2XGT 2SFP+ Switch | RUCKUS ICX 7150-48
Ports | 48* GE RJ45 6* 10G SFP+ | 48* GE RJ45 2* 10G RJ45 4* 10G SFP+ | 48* GE RJ45 4* 10G SFP+ | 44* GE RJ45, 4* GE RJ45/SFP Combo 2* 10G RJ45/SFP+ Combo 1 expansion slot (max 2* 10G SFP+） | 48* GE RJ45 4* 10G SFP+ | 48* GE RJ45 2* 10G RJ45 2* 10G SFP+ | 50* GE RJ45 4* 10G SFP+
Console Port | 1* RJ45 + 1* USB Type-C | 1* RJ45 | 1* RJ45 | 1* RS232 + 1* Mini-USB | × | × | 1* RJ45 + 1* USB Type-C
Management Port | 1* RJ45 | 1* RJ45 | × | × | × | × | 1* RJ45
USB Ports | 2* USB2.0 | 1* USB2.0 | 1* USB2.0 | 1* USB2.0 | × | × | 1* USB2.0
Packet Buffer Memory | 3 MB | 4 MB | 3 MB | 4 MB | 2 MB | 1.5 MB | 4 MB
MAC Address | 32K | 16K | 16K | 32K | 16K | 16K | 16K
Flash | 8 MB Nor + 8 GB EMMC | N/A | 256 MB | 128 MB | 256 MB | 512MB NAND | 2 GB
DRAM | 4 GB DDR4 | N/A | 512 MB | 512 MB | N/A | 1GB DDR3 | 1 GB
CPU | Dual-core @1.5GHz | N/A | 800 MHz | 800 MHz | N/A | Single-Core @800MHz | N/A
Redundant Power Supply | 2 fixed Power Supply module | Need external PSU | × | Need external PSU | × | × | ×
FAN | 4 fixed Fans | 2 fixed Fans | 1 fixed Fan | Fixed Fan | 1 fixed Fan | Fixed Fan | Fanless
Stacking Ports | 6 (the uplink ports can also use as stacking ports) | 4 | 4 | 4 (the uplink ports can also use as stacking ports) | × | 4 | 4 (the uplink ports can also use as stacking ports)
Stacking Number | 4 units per stack (Will support to 8 by FW upgrade at end of 24.Q1) | 6 units per stack | 4 units per stack | 8 units per stack | × | 4 units per stack | 12 units per stack
Entries | 2K IGMP groups | 1K IGMP groups | N/A | 2K IGMP groups | N/A | N/A | N/A
 | 64 groups LAG | 32 groups LAG | 8 groups LAG | 64 groups LAG | 16 groups LAG | N/A | N/A
 | 1K static IGMP groups | 128 static IGMP groups | N/A | N/A | N/A | N/A | N/A
 | 4K MLD Groups | 1K MLD Groups | N/A | N/A | N/A | N/A | N/A
 | 8K ARP Entries | 2K ARP Entries | N/A | 6K ARP Entries | N/A | N/A | 4K ARP Entries
 | 256 IP interfaces | 16 IP interfaces | 128 IP interfaces | 128 IP interfaces | N/A | N/A | N/A
 | 8K IPv6 ND Entries | 1K IPv6 ND Entries | N/A | N/A | N/A | N/A | N/A
 | 16K hardware routing | 3K hardware routing | N/A | 12K hardware routing | N/A | N/A | 6K hardware routing
 | 1024 Static Route | 512 Static Route | 990 static routes | 1024 Static Route | N/A | 32 Static Route | N/A
L3 Routing | Static Route, RIP, OSPF, ECMP | Static Route, PBR, RIP, OSPF, ECMP | Static Route, PBR, RIP | Static Route, RIP, OSPF, ECMP | Static Route, RIP, OSPF | Static Route | Static Route, RIP, ECMP (OSPF, PBR with license)
VRRP | √ | √ | × | √ | × | × | √ (with license)
Multicast Routing | PIM-DM (Will support PIM-SM by FW upgrade at end of 24.Q1) | PIM-SM | × | PIM-SM, PIM-DM | × | × | PIM-SM, PIM-SSM, PIM-DM (with license)
ERPS | √ | √ | × | × | × | × | ×

## Slide 6
Vendor | TP-Link | UBNT | D-Link | MikroTik
Model | SX3016F v1 | US-16-XG | DXS-1100-16SC | CRS317-1G-16S+RM
Ports | 16* 10G SFP+ | 12* SFP+ + 4* 10GE | 14* SFP+ + 2* 10GE/SFP+ Combo | 1* GE + 16* 10G SFP+
SDN Support | √ | √ | × | ×
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | 1* RJ45
MAC Address Table | 32K | - | 16K | 32K
Packet Buffer | 3 MB | - | 2 MB | 3 MB
ACL | √ | √ | √ | √
QoS | √ | √ | √ | √
Multicast | √ | √ | √ | √
VLAN | √ | √ | √ | √
Static routing | 48 (IPv4, IPv6) | × | × | √
IP interfaces | 16 | × | × | √
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | × | √
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS | × | × | √
Redundant power supply | √ | √ | × | √
Power Supply | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50-60 Hz 48/24 VDC | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50/60 Hz
Max. Power Consumption | 32.7 W | 36 W | 60 W | 44 W
FAN | 1 Fixd | 1 Fixed | 2 Fixed | 2 Flexible
Product comparison (10G Fiber Switch---- SX3016F)

## Slide 7
Vendor | TP-Link | UBNT | MikroTik
Model | SX3008F v1 | USW-Aggregation | CRS309-1G-8S+IN
Ports | 8* 10G SFP+ | 8* 10G SFP+ | 1* GE + 8* 10G SFP+
SDN Support | √ | √ | ×
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1*RB232
MAC Address Table | 32K | - | 32K
Packet Buffer | 2 MB | - | 2 MB
ACL | √ | √ | √
QoS | √ | √ | √
Multicast | √ | √ | √
VLAN Type | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | - | 802.1Q Tagged VLAN MAC VLAN Voice VLAN
Static routing | 48 (IPv4, IPv6) | × | √
IP interfaces | 16 | × | √
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | DHCP Server DHCP Snooping DHCP Relay
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS | × | OAM/ DDM/ sFlow
Casing & Installation | Metal & Rackmount | Plastic & Desktop | Metal & Rackmount
Power Supply | 100-240 VAC, 50/60 Hz | 100-240 VAC, 50/60 Hz | 802.3at PoE in; 12-57 VDC Adaptor
Max. Power Consumption | 15.5 W | 30 W | 23 W
Dimensions | 440 × 180 × 44 mm (上机架) | 440 × 120 × 44 mm (上机架) | 272 × 191 × 44 mm (上机架)
Product comparison (10G Fiber Switch---- SX3008F)

## Slide 8
Product comparison (2.5G PoE Switch---- SG3428XPP-M2)
Vendor | TP-Link | UBNT | Zyxel
Model | SG3428XPP-M2 | USW-Enterprise-24-PoE | XMG1930-30HP
Ports | 24* 2.5Gbps RJ45 4* 10Gbps SFP+ | 12* GE RJ45 12* 2.5Gbps RJ45 2* 10Gbps SFP+ | 24* 2.5Gbps RJ45 4* 10Gbps RJ45 2* 10Gbps SFP+
Management Ports | 1* RJ45 Console + 1* Micro-USB Console | × | ×
PoE budget | 8* 2.5G PoE++ Ports (up to 60W per port) ； 16* 2.5G PoE+ Ports； total PoE power budget为500W | 12* 2.5G PoE+ Ports； 12* GE PoE+ Ports； total PoE power budget为400W | 4* 10G PoE++ Ports (up to 60W per port)； 4* 2.5G PoE++ Ports (up to 60W per port)； 20* 2.5G PoE+ Ports； total PoE power budget为700W
Packet Buffer | 2 MB | - | 2 MB
MAC Address | 32K | - | 16K
Flash / RAM | 32 MB / 256 MB | - | 32 MB / 256 MB
IP Interface | 32 | √ | 32
Centralized Management | √（Omada SDN） | √（Unifi） | √（Nebula）
Static route | √ | √ | √
DHCP Server | √ | √ | ×
CLI | √ | - | 需单独购买License

## Slide 9
Product comparison (2.5G Switch---- SG3428X-M2)
Vendor | TP-Link | Zyxel
Model | SG3428X-M2 | XMG1930-30
Ports | 24* 2.5Gbps RJ45 4* 10Gbps SFP+ | 24* 2.5Gbps RJ45 4* 10Gbps RJ45 2* 10Gbps SFP+
Management Ports | 1* RJ45 Console + 1* Micro-USB Console | -
Packet Buffer | 2 MB | 2 MB
MAC Address | 32K | 16K
Flash / RAM | 32 MB / 256 MB | 32 MB / 256 MB
IP Interface | 32 | 32
Centralized Management | √（Omada SDN） | √（Nebula）
Static route | √ | √
DHCP Server | √ | ×
CLI | √ | 需单独购买License
Max. power consumption | 45.1 W | 67.1 W
Dimensions | 17.3 × 7.1 × 1.7 in (440 × 180 × 44 mm) | 17.3 × 10.6 × 1.7 in (441 × 270 × 44 mm)

## Slide 10
Vendor | TP-Link | D-Link | NetGear | Trendnet
Model | SG3210XHP-M2 v3 | DMS-1100-10TP | M4200-10MG-PoE+ | TPE-30102WS
Ports | 8* 2.5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+ | 6* 2.5G RJ45 + 2* 5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+
SDN Support | √ | × | × | ×
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB | 1* RJ45
MGMT Ports | × | × | 1 | ×
USB Ports | × | × | 1 | ×
PoE | 8 PoE+, 240 W | 8 PoE+, 240 W | 8 PoE+, 240 W | 8 PoE+, 240 W
MAC Address Table | 16K | 16K | 16K | 32K
Packet Buffer | 12 Mbit | - | 16 Mbit | 16 Mbit
ACL | √ | √ | √ | √
QoS | √ | √ | √ | √
Multicast | √ | √ | √ | √
VLAN Type | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | 802.1Q Tagged VLAN MAC VLAN Voice VLAN | 802.1Q Tagged VLAN MAC VLAN Protocol VLAN Private VLAN Voice VLAN | 802.1Q Tagged VLAN Private VLAN Voice VLAN
Static routing | 48 (IPv4, IPv6) | × | 32 IPv4, 32 IPv6 | 32 (IPv4, IPv6)
RIP dynamic routing | × | × | 32 IPv4 | ×
IP interfaces | 16 | × | 64 | 8
DHCP | DHCP Server DHCP Snooping DHCP Relay | × | DHCP Server DHCP Snooping DHCP Relay | DHCP Server DHCP Snooping DHCP Relay
TLS Version | 1.2 | 1.2 | 1.0 | 1.2
LAG Groups | 8 Groups | 8 Groups | 5 Groups | 4 Groups
ISP Feature | OAM/ DDM/ L2TP/ sFlow ERPS | ERPS | sFlow | ×
Casing & Installation | Metal & Rackmount | Metal & Rackmount | Metal & Rackmount | Metal & Rackmount
Product comparison (2.5G PoE Switch---- SG3210XHP-M2)

## Slide 11
Product comparison (24 SFP Switch with 10G Uplink---- SG3428XF)
Vendor | TP-Link | D-Link | MikroTik
Model | SG3428XF v1 | DGS-1210-28XS/ME | CRS328-4C-20S-4S+RM
Port | 20 SFP + 4 SFP/RJ45 Combo + 4 SFP+ | 24 SFP + 4 SFP+ | 20 SFP + 4 SFP/RJ45 Combo + 4 SFP+
Console | 1 RJ45 + 1 Micro-USB | 1 RJ45 | 1 RJ45
SDN support | √ | × | ×
MAC Address | 16K | 16K | 16K
Packet Buffer | 1.5MB | 1.5MB | 1.5MB
Flash | 32MB | 32MB | 16MB
RPS | √ | × | √
Fan | 1 | 1 | 2
VLAN Group | 4K | 4K | √
IP Interface | 16 | — | √
Static route | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | √
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | DHCP Server, DHCP Relay, DHCP Snooping | √
ISP Feature* | OAM, L2TP, DDM, sFlow, ERPS | OAM, DDM, Dying Gasp | √
Advance Feature | × | × | √（RIP、OSPF、BGP）

## Slide 12
Product comparison (48 GE Switch with 10G Uplink---- SG3452X)
Vendor | TP-Link | UBNT | D-Link | NetGear | Aruba
Model | SG3452X v1 | USW-Pro-48 | DGS-3000-52X | GC752X | 2540 48G 4SFP+ Switch
Port | 48 RJ45 + 4 SFP+ | 48 RJ45 + 4 SFP+ | 48 RJ45 + 4 SFP+ | 48 RJ45 + 2 SFP + 2 SFP+ | 48 RJ45 + 4 SFP+
Console | 1 RJ45 + 1 Micro-USB | × | 1 RJ45 | 1 Micro-USB | 1 RJ45 + 1 Micro-USB
SDN support | √ | √ | × | √ | √
MAC Address | 16K | √ | 16K | 16K | 16K
VLAN Group | 4K | √ | 4K | 256 | 512
IP Interface | 16 | √ | 16 | 15 | -
Static route | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | 256 (IPv4, IPv6)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | DHCP Server | DHCP Server, DHCP Relay, DHCP Snooping | DHCP snooping | DHCP Server, DHCP Relay
ISP Feature* | OAM, L2TP, DDM, sFlow | × | OAM, L2TP, sFlow, Dying Gasp, CFM, Y.1731 OAM | × | sFlow
USB | × | × | × | 1 | ×
RPS | × | √ | √ | × | ×
Max. power consumption | 32.7W | 60W | 40.7W | 43.9W | 46.6W
Fan | 无 | 无 | 2 | 1 | 1

## Slide 13
Product comparison (48 GE PoE Switch with 10G Uplink---- SG3452XP)
Vendor | TP-Link | UBNT | D-Link | NetGear | Aruba
Model | SG3452XP v2 | US-48-500W | DGS-1250-52XMP | GC752XP | 2540 48G PoE+ 4SFP+ Switch
Port | 48 RJ45 + 4 SFP+ | 48 RJ45 + 2 SFP + 2 SFP+ | 48 RJ45 + 4 SFP+ | 48 RJ45 + 2 SFP + 2 SFP+ | 48 RJ45 + 4 SFP+
Console | 1 RJ45 + 1 Micro-USB | 1 RJ45 | 1 RJ45 | 1 Micro-USB | 1 RJ45 + 1 Micro-USB
SDN support | √ | √ | × | √ | √
MAC Address | 16K | 16K | 32K | 16K | 16K
PoE budget | 48 PoE+, 500W | 48 PoE+,436W | 48 PoE, 370W | 48 PoE+ , 505W | 48 PoE+, 370W
VLAN Group | 4K | 255 | 4K | 256 | 512
IP Interface | 16 | × | 4 | 15 | -
Static route | 48 (IPv4, IPv6) | × | 124 IPv4, 50 IPv6 | 32 IPv4, 31 IPv6 | 256 (IPv4, IPv6)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | × | DHCP Relay, DHCP Snooping | DHCP snooping | DHCP Server, DHCP Relay
ISP Feature* | OAM, L2TP, DDM, sFlow, ERPS | × | OAM | × | sFlow
USB | × | × | × | 1 | ×

## Slide 14
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | SG3428XMP v3 | USW-Pro-24-PoE | DGS-3000-28XMP | GC728XP | MS125-24P-HW | 2540 24G PoE+ 4SFP+ Switch
Ports | 24* GE + 4* 10G SFP+ | 24* GE + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 2* SFP + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 4* 10G SFP+
SDN Support | √ | √ | × | √ | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 24 PoE+, 384 W | 16 PoE+, 8 PoE++, 400 W | 24 PoE+, 370 W | 24 PoE+, 390 W | 24 PoE+, 370 W | 24 PoE+, 370 W
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 36 Mbit Ingress 62.2 Mbit Egress
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | - | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
AAA | √ | - | √ | √ | √ | √
IP interfaces | 16 | - | 16 | 15 | × | -
Static routing | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | × | 256 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Server | DHCP Server DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay | DCHP Server DHCP Relay
ISP Feature | OAM/ L2TP/ DDM/ sFlow ERPS | × | OAM/ L2TP/ sFlow | × | × | sFlow
Product comparison (24 GE PoE Switch with 10G Uplink---- SG3428XMP)

## Slide 15
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | SG3428X v1.20 | USW-Pro-24 | DGS-3000-28X | GC728X | MS125-24-HW | 2540 24G 4SFP+ Switch
Ports | 24* GE + 4* 10G SFP+ | 24* GE + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 2* SFP + 2* 10G SFP+ | 24* GE + 4* 10G SFP+ | 24* GE + 4* 10G SFP+
SDN Support | √ | √ | × | √ | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
MAC Address Table | 16K | - | - | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 36 Mbit Ingress 62.2 Mbit Egress
ACL | √ | √ | √ | √ | √ | √
QoS | √ | √ | - | √ | √ | √
LAG | √ | √ | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | - | √ | √ | √ | √
802.1x | √ | - | √ | √ | √ | √
STP | √ | - | √ | √ | √ | √
AAA | √ | - | √ | √ | √ | √
IP interfaces | 16 | - | 16 | 15 | × | -
Static routing | 48 (IPv4, IPv6) | √ | 64 IPv4, 32 IPv6 | 32 IPv4, 31 IPv6 | × | 256 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Server DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay | DCHP Server DHCP Relay
ISP Feature | OAM/ L2TP/ DDM/ sFlow ERPS | - | OAM/ L2TP/ sFlow | × | × | sFlow
Product comparison (24 GE Switch with 10G Uplink---- SG3428X)

## Slide 16
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | SG3452P v3.20 | USW-48-PoE | DGS-1210-52MP/ME | GS752TPv2 | MS120-48LP-HW | 2530-48G-PoE+ Switch
Ports | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP | 50* GE + 2* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 | × | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 48 PoE+, 384W | 32 PoE+, 195W | 40 PoE, 8 PoE+, 370W | 48 PoE+, 380W | 48 PoE+, 370W | 48 PoE+, 382W
MAC Address Table | 16K | - | 16K | 16K | 32K | 16K
Packet Buffer | 12 Mbit | - | 24 Mbit | 12 Mbit | - | 24 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 16 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 15 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 32 IPv4, 32 IPv6 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | × | × | OAM, DDM, Dying Gasp, ERPS | × | × | sFlow
Product comparison (48 GE PoE Switch---- SG3452P)

## Slide 17
Vendor | TP-Link | D-Link | NetGear | Meraki | Aruba
Model | SG3452 v1 | DGS-1210-52/ME | GS748Tv5 | MS120-48-HW | 2530-48G Switch
Ports | 48* GE + 4* SFP | 48* GE + 4* SFP | 46* GE + 2 GE/SFP Combo + 2* SFP | 48* GE + 4* SFP | 48* GE + 4* SFP
SDN Support | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | × | 1* RJ45 + 1* Micro-USB
RPS | × | √ | × | × | ×
MAC Address Table | 16K | 16K | 16K | 32K | 16K
Packet Buffer | 12 Mbit | 24 Mbit | 12 Mbit | - | 24 Mbit
ACL | √ | √ | √ | √ | √
QoS | √ | √ | √ | √ | √
VLAN Group | 4K | 4K | 256 | 4K | 512
Multicast | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √
AAA | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 16 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | × | 15 | × | ×
Static routing | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | 32 IPv4, 32 IPv6 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP snooping Layer 2 DHCP Relay | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | × | OAM, DDM, Dying Gasp, ERPS | × | × | sFlow
Product comparison (48 GE Switch---- SG3452)

## Slide 18
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | SG3428MP v6 | US-24-500W | DGS-1210-28MP/ME | M4100-26G-PoE | MS120-24P-HW | 2530-24G-PoE+ Switch
Ports | 24* GE + 4* SFP | 24* GE + 2* SFP | 24* GE + 4* SFP | 24* GE + 2* GE/SFP Combo + 2* SFP | 24* GE + 4* SFP | 26* GE + 2* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | 1* RJ45 | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
PoE | 24 PoE+, 384W | 24 PoE+, 470W | 24 PoE+, 370W | 24 PoE+, 380W | 24 PoE+, 370W | 24 PoE+, 195W
RPS | × | × | × | √ | × | ×
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 12 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 1K | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 12 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 64 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 64 IPv4 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM, sFlow ERPS | × | OAM, DDM, Dying Gasp, ERPS | sFlow | × | sFlow
Product comparison (24 GE PoE Switch---- SG3428MP)

## Slide 19
Vendor | TP-Link | UBNT | D-Link | NetGear | Meraki | Aruba
Model | SG3428 v2.20 | US-24 | DGS-1210-28/ME | M4100-26G | MS120-24-HW | 2530-24G Switch
Ports | 24* GE + 4* SFP | 24* GE + 2* SFP | 24* GE + 4* SFP | 24* GE + 2* GE/SFP Combo + 2* SFP | 24* GE + 4* SFP | 24* GE + 4* SFP
SDN Support | √ | √ | × | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | 1* RJ45 | 1* RJ45 + 1* Micro-USB | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1 | × | ×
RPS | × | × | √ | √ | × | ×
MAC Address Table | 16K | - | 16K | 16K | 16K | 16K
Packet Buffer | 12 Mbit | - | 12 Mbit | 12 Mbit | - | 12 Mbit
ACL | √ | √ | √ | √ | √ | √
QoS | √ | - | √ | √ | √ | √
VLAN Group | 4K | - | 4K | 1K | 4K | 512
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √ | √
LAG Groups | 8 Groups | - | 8 Groups | 12 Groups | 8 Groups | 8 Groups
IP interfaces | 16 | - | × | 64 | × | ×
Static routing | 48 (IPv4, IPv6) | - | 64 IPv4, 32 IPv6 | 64 IPv4 | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | - | DHCP Relay DHCP Snooping | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM, sFlow ERPS | × | OAM, DDM, Dying Gasp, ERPS | sFlow | × | sFlow
Product comparison (24 GE Switch---- SG3428)

## Slide 20
Vendor | TP-Link | D-Link | NetGear | Aruba
Model | SG3210 v3 | DGS-1210-10/ME | GC110 | 2530-8G Switch
Ports | 8* GE + 2* SFP |  |  | 
SDN Support | √ | × | √ | √
Console Ports | 1* RJ45 + 1* Micro-USB | 1* RJ45 | × | 1* RJ45 + 1* Micro-USB
RPS | × | √ | × | ×
MAC Address Table | 8K | 16K | 16K | 16K
Packet Buffer | 4.1 Mbit | 12 Mbit | 12 Mbit | 12 Mbit
ACL | √ | √ | √ | √
QoS | √ | √ | √ | √
VLAN Group | 4K | 4K | 1K | 512
Multicast Group | 511 | 256 | 512 | -
ARP | 316 | 256 | 384 | -
802.1x | √ | √ | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 5 Groups | 8 Groups
IP interfaces | 16 | × | 15 | ×
Static routing | 48 (IPv4, IPv6) | 64 IPv4, 32 IPv6 | 64 IPv4 | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Snooping | DHCP Snooping
ISP Feature | OAM, DDM | OAM, DDM, Dying Gasp, ERPS | × | sFlow
Installation | Desktop, Rackmount | Desktop, Rackmount | Desktop, Wall-mount | Desktop, Rackmount
Product comparison (8 GE Switch---- SG3210)

## Slide 21
Vendor | TP-Link | D-Link | NetGear | Cisco
Model | SG2428P v6 | DBS-2000-28P | GS728TP | CBS250-24P-4G
Ports | 24* GE + 4* SFP | 24* GE + 4* GE/SFP Combo | 24* GE + 4* SFP | 24* GE + 4* SFP
SDN Support | √ | √ | × | ×
Console Ports | × | 1* RJ45 | × | 1* RJ45 + 1* Micro-USB
USB Ports | × | × | × | 1
PoE | 24 PoE+, 250W | 24 PoE+, 193W | 16 PoE, 8 PoE+, 192W | 24 PoE+, 195W
MAC Address Table | 8K | 8K | 8K | 8K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 8 Mbit | 8 Mbit
ACL | √ | √ | √ | √
QoS | √ | × | √ | √
VLAN Group | 4K | 256 | 256 | 255
Multicast | √ | √ | √ | √
802.1x | √ | × | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 8 Groups | 4 Groups
IP interfaces | 16 | × | 32 | 16
Static routing | 32 (IPv4, IPv6) | × | 32 IPv4 | 32 IPv4
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | DHCP Snooping | DHCP Relay
Product comparison (24 GE PoE Smart Switch---- SG2428P)

## Slide 22
Model | Omada SG2428LP | UBNT USW-24-POE (95W)
Port | 24* GE + 4* SFP | 24* GE + 2* SFP
PoE | 16* PoE+, 150W PoE Budget | 16* PoE+, 95W PoE Budget
Button | 1* Reset | 1* Reset
Total non-blocking throughput | 28 Gbps | 26 Gbps
Forwarding rate | 41.66 Mpps | 38.69 Mpps
Static Routing | √ | ×
IP Interface | √ | ×
DHCP Server | √ | ×
DHCP Relay | √ | ×
Surge | 6 kV for port and 4 kV for power module | N/A
FAN | Fanless | Fanless
Power method | 100—240V AC, 50/60 Hz | 100—240V AC, 50/60 Hz
Product comparison (24 GE PoE Smart Switch---- SG2428LP)

## Slide 23
Product comparison (16 GE PoE Smart Switch---- SG2218P)
Vendor | TP-Link | UBNT | NetGear | Cisco
Model | SG2218P v1 | USW-16-PoE | GS716TP | CBS250-16P-2G
Ports | 16* Gigabit RJ45 Ports + 2* Gigabit SFP Slots |  |  | 
PoE ports | 16* PoE+, max 30W/port | 8* PoE+, max 30W/port | 16* PoE, max 30W/port | 16* PoE, max 30W/port
PoE budget | 150W | 42W | 180W | 120W
Packet Buffer | 4.1 Mbit | - | 12 Mbit | 12 Mbit
MAC Address | 8K | - | 16K | 8K
VLAN Group | 4K | - | 256 | 255
SDN Support | √ | √ | √ | ×
IP Interface | 16 | × | × | 16
Static route | 32 (IPv4, IPv6) | × | × | 32 (IPv4, IPv6)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | × | DHCP Snooping | DHCP Relay
Dimensions | 17.3 × 7.1 × 1.7 in (440 × 180 × 44 mm) | 17.4 × 7.9 × 1.7 in (442 × 200 × 44 mm) | 17.3 × 8.0 × 1.7 in (440 × 204 × 43 mm) | 10.6 × 11.7 × 1.7 in (268 × 297 × 44 mm)
Fan | 1 | Fanless | 1 | Fanless

## Slide 24
Vendor | TP-Link | D-Link | NetGear | Aruba
Model | SG2218 v1 | DGS-1210-20 | GS716Tv3 | 1920 16G Switch
Ports | 16* GE + 2* SFP | 16* GE + 4* SFP | 16* GE + 2* SFP | 16* GE + 4* SFP
SDN Support | √ | × | × | ×
Console Ports | × | × | × | 1* RJ45
MAC Address Table | 8K | 8K | 16K | 8K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 2 Mbit | 4.1 Mbit
ACL | 230 | 200 | 100 | -
ARP | 316 | 128 | 512 | -
QoS | √ | × | √ | √
VLAN Group | 4K | 256 | 256 | 4K
Multicast | √ | √ | √ | √
802.1x | √ | × | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 26 Groups | 8 Groups
IP interfaces | 16 | × | 15 | 8
Static routing | 32 (IPv4, IPv6) | × | 32 IPv4 | 32 (IPv4, IPv6)
DHCP | DHCP Server DHCP Relay DHCP Snooping | DHCP Snooping | DHCP Snooping | DHCP Relay
Product comparison (16 GE Smart Switch---- SG2218)

## Slide 25
Product comparison (16 GE Smart PoE Switch---- SG2016P)
Vendor | TP-Link | UBNT | NetGear
Model | SG2016P v1 | USW-Lite-16-PoE | GS516TP
Ports | 16* GE + 2* SFP | 16* GE + 4* SFP | 16* GE + 2* SFP
Ports | 16* Gigabit RJ45 | 16* Gigabit RJ45 | 16* Gigabit RJ45
PoE ports | 8* PoE+, max 30W/port | 8* PoE+, max 30W/port | 8* PoE, max 15.4W/port
PoE budget | 120W | 45W | 76W
MAC Address | 8K | - | 8K
VLAN Group | 4K | - | 256
SDN Support | √ | √ | ×
IP Interface | 16 | × | √
Static route | 32 (IPv4, IPv6) | × | 32 (IPv4)
DHCP | DHCP Server, DHCP Relay, DHCP Snooping | × | DHCP Snooping
Dimensions | 286*111.7*25.4 mm | 191.7*185*43.7 mm | 328*169*43 mm
Fan | × | × | √
Power Supply | 53.5VDC/2.43A | 100-240V AC | 100-240V AC
Mounting | Desktop/ Wall-mount | Desktop | Rackmount

## Slide 26
Product comparison (8 2.5G Smart PoE Switch----SG2210XHP-M2)
Vendor | TP-Link | UBNT | NetGear
Model | SG2210XMP-M2 | USW-Enterprise-8-PoE | MS108EUP
Ports | 8* 2.5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45 + 2* 10G SFP+ | 8* 2.5G RJ45
PoE ports | 8* PoE+, max 30W/port | 8* PoE+, max 30W/port | 4* PoE++, max 60W/port 4* PoE+ in, max 30W/port
PoE Budget | 160W | 120W | 230W
SDN Support | √ | √ | ×
MAC Address | 16k | - | 16k
Packet buffer | 1.5 MB | - | 1.5 MB
IP Interface | 32 | × | ×
Static route | 32 (IPv4, IPv6) | × | ×
DHCP | ●DHCP Server ●DHCP Relay ●DHCP Snooping | × | ×
AAA | √ | × | ×
IGMP Snooping | √ | × | √
STP | √ | × | ×
Port Security | √ | × | ×
CLI | √ | × | ×
Power Supply | External Power Adapter, 53.5VDC/3.37A input | Internal Power module, AC input | External Power Adapter
Dimensions | 226 × 131 × 35 mm | 200 × 248 × 44 mm | 210 × 140 × 40 mm
FAN | Fanless | Fanless | Fanless
Shell material | Steel | Plastic | Steel
Mounting | Desktop/Wall-Mounting | Desktop | Desktop/Wall-Mounting

## Slide 27
Vendor | TP-Link | UBNT | D-Link | NetGear | Aruba | Meraki
Model | SG2210MP v4 | US-8-150W | DBS-2000-10MP | GS510TP | 1920 8G PoE+ (180W) switch | MS120-8FP-HW
Ports | 8* GE + 2* SFP |  |  |  |  | 
SDN Support | √ | √ | √ | × | × | √
Console Ports | × | × | × | × | 1* RJ45 | ×
PoE | 8 PoE+, 150W | 8 PoE+, 130W | 8 PoE+, 130W | 8 PoE+, 130W | 8 PoE+, 180W | 8 PoE+, 124W
Fan | 1 | × | × | 1 | 1 | ×
MAC Address Table | 8K | 16K | 8K | 4K | 8K | 16K
Packet Buffer | 4.1 Mbit | - | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | -
QoS | √ | - | × | √ | √ | √
VLAN Group | 4K | 255 | 256 | 64 | 4K | 4K
Multicast | √ | √ | √ | √ | √ | √
802.1x | √ | √ | × | √ | √ | √
STP | √ | - | √ | √ | √ | √
LAG Groups | 8 Groups | 6 Groups | - | - | 4 Groups | -
IP interfaces | 16 | × | × | × | 8 | ×
Static routing | 32 (IPv4, IPv6) | × | × | × | 32 (IPv4, IPv6) | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | × | DHCP Relay | DHCP Relay DHCP Snooping
Installation | Desktop, Rackmount | Desktop | Desktop, Rackmount | Desktop, Rackmount | Desktop, Rackmount | Desktop, Wall-mount
Product comparison (8 GE Smart PoE Switch---- SG2210MP)

## Slide 28
Vendor | TP-Link | D-Link | NetGear | Aruba | Meraki
Model | SG2210P v5 | DGS-1210-10P | GS110TPv3 | 1920 8G PoE+ (65W) switch | MS120-8LP-HW
Ports | 8* GE + 2* SFP |  |  |  | 
SDN Support | √ | × | × | × | √
Console Ports | × | × | × | 1* RJ45 | ×
PoE | 8 PoE+, 61W | 8 PoE+, 65W | 8 PoE, 46W | 8 PoE+, 65W | 8 PoE+, 67W
Fan | × | × | 1 | × | ×
MAC Address Table | 8K | 8K | 4K | 8K | 16K
Packet Buffer | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | 4.1 Mbit | -
QoS | √ | × | √ | √ | √
VLAN Group | 4K | 256 | 64 | 4K | 4K
Multicast | √ | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √
STP | √ | √ | √ | √ | √
LAG Groups | 8 Groups | 4 Groups | - | 4 Groups | -
IP interfaces | 16 | × | × | 8 | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 (IPv4, IPv6) | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | DHCP Relay | DHCP Relay DHCP Snooping
Installation | Desktop, Wall-mount | Desktop, Rackmount | Desktop, Wall-mount | Desktop, Rackmount | Desktop, Wall-mount
Product comparison (8 GE Smart PoE Switch---- SG2210P)

## Slide 29
Vendor | TP-Link | UBNT |  | HPE
Model | SG2008P v3 | USW-Lite-8-PoE | US-8-60W | 1920S 8G PPoE+ 65W Switch
Ports | 8* GE |  |  | 
SDN Support | √ |  |  | ×
PoE | 4 PoE+, 62W | 4 PoE+, 52W | 4 PoE, 48W | 4 PoE+, 65W
PoE Standard | 802.3af/at | 802.3af/at | 802.3af | 802.3af/at
Fan | × |  |  | 
MAC Address Table | 8K | - | - | 8K
Packet Buffer | 4.1 Mbit | - | - | 12 Mbit
QoS | √ | - | - | √
VLAN Group | 4K | - | - | 4K
Multicast | √ | - | - | √
802.1x | √ | √ | √ | √
STP | √ | - | - | √
LAG Groups | 8 Groups | - | - | 4 Groups
IP interfaces | 16 | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 IPv4
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | DHCP Relay
Installation | Desktop, Wall-mount |  |  | Rackmount
Shell material | Metal | Plastic | Metal | Metal
Product comparison (8 GE Smart PoE Switch---- SG2008P)

## Slide 30
Vendor | TP-Link | UBNT | Meraki | NetGear | Aruba | D-Link
Model | SG2008 v4 | US-8 | MS120-8-HW | GS108Tv3 | 1920S 8G Switch | DGS-1210-10
Ports | 8* GE | 8* GE | 8* GE + 2* SFP | 8* GE | 8* GE | 8* GE + 2* SFP
SDN Support | √ | √ | √ | √ | × | ×
MAC Address Table | 8K | - | 16K | 8K | 8K | 8K
Packet Buffer | 4.1 Mbit | - | - | 4.1 Mbit | 12 Mbit | 4.1 Mbit
QoS | √ | - | √ | √ | √ | ×
VLAN Group | 4K | - | 4K | 64 | 4K | 256
Multicast | √ | - | √ | √ | √ | √
802.1x | √ | √ | √ | √ | √ | √
STP | √ | - | √ | √ | √ | √
LAG Groups | 8 Groups | - | - | 8 Groups | 4 Groups | 4 Groups
IP interfaces | 16 | × | × | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | 32 IPv4 | 32 IPv4 | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | DHCP Relay DHCP Snooping | DHCP Relay DHCP Snooping | DHCP Relay | ×
Power Supply | 12 V/1 A DC PoE in | 48 V/0.5 A DC PoE in | 54 V/1.67 A DC | 12 V/1 A DC PoE in | 100-240 V AC ~ 50/60 Hz | 100-240 V AC ~ 50/60 Hz
PoE Passthrough | × | √ (12W) | × | × | × | ×
Installation | Desktop, Wall-mount | Desktop, Wall-mount | Desktop, Wall-mount | Desktop, Rackmount | Rackmount | Desktop, Rackmount
Product comparison (8 GE Smart Switch---- SG2008)

## Slide 31
Product comparison (5 GE Smart Switch----SG2005P-PD)
Vendor | TP-Link | UBNT
Model | SG2005P-PD | USW-Flex
Ports | 5* GE | 5* GE
PoE ports | 1* PoE++ in, max 90W/port 4* PoE++ in, max 30W/port | 1* PoE++ in, max 90W/port 4* PoE++ in, max 30W/port
Flash | 32 MB | -
DRAM | 256 MB | 128 MB
PoE budget | 64 W when powered by 802.3bt Type 4 (90 W) 44 W when powered by 802.3bt Type 3 (60 W) 19 W when powered by 802.3at 6 W when powered by 802.3at | 46 W when powered by 802.3bt Type 3 (60 W) 20 W when powered by 802.3at 8 W when powered by 802.3at
MAC Address | 8K | -
VLAN Group | 4K | -
SDN Support | √ | √
IP Interface | 16 | ×
Static route | 32 (IPv4, IPv6) | ×
DHCP | ●DHCP Server ●DHCP Relay ●DHCP Snooping | ×
AAA | √ | ×
LACP | √ | ×
IGMP Snooping | √ | ×
STP | √ | ×
DHCP Filter | √ | ×
Port Security | √ | ×
ACL | √ | ×
Auto VoIP | √ | ×
CLI | √ | ×
IP | IP55 | IP55
Surge Protection | 4kV | ×
Dimensions | 170 × 100 × 38.5 mm | 122.5 x 107.1 x 28 mm
FAN | Fanless | Fanless
Operating Temperature | -40 to 60 °C | -40 to 55° C
Shell material | Plastic | Plastic
Mounting | Pole-Mounting/Wall-Mounting | Pole-Mounting/Wall-Mounting

## Slide 32
Product comparison (8 GE Smart PoE Switch)
Vendor | TP-Link |  | 
Model | SG2008P v1/v2 | SG2210P v3.2/v4 | SG2210MP v1/v2
Ports | 8* GE | 8* GE + 2* SFP | 
SDN Support | √ |  | 
PoE | 4 PoE+, 62W | 8 PoE+, 61W | 8 PoE+, 150W
Average PoE power / port | 15.5W | 7.6W | 18.7W
IP interfaces | 16 |  | 
Static routing | 32 (IPv4, IPv6) |  | 
DHCP | DHCP Server DHCP Relay DHCP Snooping |  | 
Installation | Desktop, Wall-mount |  | Desktop, Rackmount
FAN | × |  | 1
Features | 单端口平均PoE功率为15.5W，高于11ac EAP，即4个PoE端口可同事连接11ac EAP; 4个非PoE端口可用于下连有线设备； 桌面型无风扇设计，部署灵活，可用于家用、办公等场景； | 8个PoE口，单端口平均PoE功率为7.6W，可满载11ac面板AP； 光口可满足长距离传输需求； 桌面型无风扇设计，部署灵活，可用于家用、办公等场景； | 8个PoE口，单端口平均PoE功率为18.7W，可满载11ac EAP； 光口可满足长距离传输需求； 机架型设计，可满足中小型企业机架安装场景；
Vendor | TP-Link |  | 
Model | SG2008P v1/v2 | SG2210P v3.2/v4 | SG2210MP v1/v2
Ports | 8* GE | 8* GE + 2* SFP | 
SDN Support | √ |  | 
PoE | 4 PoE+, 62W | 8 PoE+, 61W | 8 PoE+, 150W
Average PoE power / port |  |  | 
IP interfaces | 16 |  | 
Static routing | 32 (IPv4, IPv6) |  | 
DHCP | DHCP Server DHCP Relay DHCP Snooping |  | 
Installation | Desktop, Wall-mount |  | Desktop, Rackmount
FAN | × |  | 1
Features | 单端口平均PoE功率为15.5W，高于11ac EAP，即4个PoE端口可同事连接11ac EAP; 4个非PoE端口可用于下连有线设备； 桌面型无风扇设计，部署灵活，可用于家用、办公等场景； | 8个PoE口，单端口平均PoE功率为7.6W，可满载11ac面板AP； 光口可满足长距离传输需求； 桌面型无风扇设计，部署灵活，可用于家用、办公等场景； | 8个PoE口，单端口平均PoE功率为18.7W，可满载11ac EAP； 光口可满足长距离传输需求； 机架型设计，可满足中小型企业机架安装场景；

## Slide 33
Vendor | TP-Link | NetGear | D-Link | Trendnet
Model | SL2428P v6 | FS728TP | DES-1210-28P | TPE-224WS (C1.0R)
Ports | 24* FE + 2* GE + 2* GE/SFP Combo |  |  | 
SDN Support | √ | × | × | ×
PoE | 24 PoE+, 250W | 24 PoE, 192W | 20 PoE, 4 PoE+, 193W | 20 PoE, 4 PoE+, 193W
MAC Address Table | 8K | 4K | 8K | 8K
Packet Buffer | 4.1 Mbit | 8 Mbit | 4.1 Mbit | 4.1 Mbit
QoS | √ | √ | √ | √
VLAN Group | 4K | 128 | 256 | 256
Multicast | √ | √ | √ | √
802.1x | √ | √ | √ | √
STP | √ | √ | √ | √
LAG Groups | 8 Groups | 8 Groups | 8 Groups | -
IPv6 | √ | × | √ | √
IP interfaces | 16 | × | × | ×
Static routing | 32 (IPv4, IPv6) | × | × | ×
DHCP | DHCP Server DHCP Relay DHCP Snooping | × | × | ×
IPv6 | √ | × | √ | √
Fan | 2 | 1 | 3 | 2
Product comparison (24 FE Smart Switch---- SL2428P)

## Slide 34
Product comparison (Hardware Controller---- OC400)
Model | Omada OC400 | UBNT CK-Enterprise
Management device type | Omada Networks | UniFi Networks
Management scale | 1,000 Omada EAPs + 200 Omada Switches + 100 Omada Routers; 30,000 Clients | 1,000+ UniFi Network devices; 10,000+ clients
CPU | Quad-Core A72 @ 2.2 GHz | 16-core Intel® Xeon®-SP Gold 5218 @ 2.3 GHz
Memory | 8 GB DDR4 | 32 GB DDR4
Storage | 4 MB Nor Flash + 32 GB Emmc | 256 GB M.2 2280 SATA
Management interface | 1* GE RJ45 Console Port | 1* GE RJ45 MGMT Port
Networking interface | 2* 10G SFP+ slot 4* GE RJ45 port | 1* 10G SFP+ slot 1* GE RJ45 port
USB | 2* USB 3.0 for higher storage | ×
Bluetooth | × | √ (for instant setup)
Remote centralized managed by cloud | √ | √
Power method | 100—240V AC, 50/60 Hz | 100—240V AC, 50/60 Hz
Power supply | 2* internal fixed power supply modules | 2* Hot-swappable power supply modules
FAN | 1* fixed FAN | 2 FAN at power supply modules
Surge | 4Kv protect | NA
Operating temperature | 0 to 40 °C (32 to 104 °F) | 0 to 35° C (32 to 95° F)
Dimensions | 440 × 180 × 44 mm | 481.4 × 787 × 43.7 mm
Price | Low | Very High ($4,999 at Unifi store)

## Slide 35: Business Networking
  Switch竞品对比
  Router竞品对比
35
Contents

## Slide 36
ER605 v2 vs MikroTik hEX
主要用于家用、小微企业商用场景，功能可覆盖General场景的需求；
优劣势 | 项目 | ER605 v2 | RB750Gr3 | 备注
优势 | SDN管理 | √ | × | 配置、运维更方便
 | 一键VPN | √ | × | VPN配置更方便
 | TCP性能 | ER605 v2优于RB750Gr3（各种拨号方式下双向TCP性能均比竞品高700 Mbps左右） |  | -
 | UDP报文转发率 | ER605 v2优于RB750Gr3（比竞品高750Mbps左右） |  | -
 | PPTP/L2TP VPN性能 | ER605 v2的PPTP/L2TP VPN throughput和稳定性优于竞品 |  | -
 | IPSec VPN性能 | SH1加密下的IPSec VPN性能与竞品相当，但IPSec加密算法比竞品多了SHA2 |  | 新增的SHA2增强了IPSec VPN的安全性
 | UI界面 | ER605 V2的UI界面更友好易用 |  | 降低配置难度
 | Flash容量 | 128 MB | 16 MB | ER605 v2支持双固件，产品稳定性更好
 | 壳体材质 | 钢壳 | 塑壳 | 钢壳稳定性好，散热性能好
劣势 | 连接数 | 150000 | 236000 | 在P2P下载等高连接数的应用场景下可能影响最大并发带机量，但工厂实际网络测试中，峰值带机量200-300，符合产品定位
 | 三层功能 | 静态路由，RIP, OSPF, DHCP | 含有动态路由和MPLS | 竞品的强三层功能需要单独付费购买License才能使用。由于产品定位，MPLS功能暂无规划

## Slide 37
机型 | Static IP（Mbps） |  |  |  | DHCP（Mbps） |  |  | 
 | 上行 | 下行 | 双向 | 双LAN/ WAN双向 | 上行 | 下行 | 双向 | 双LAN/ WAN双向
ER605 v2 | 945.77 | 945.56 | 1808.29 | 1535.77 | 945.93 | 945.43 | 1808.11 | 1580.52
ER605 v1 | 944.73 | 945.37 | 1816.48 | 1283.92 | 945.13 | 945.21 | 1729.48 | 1275.76
RB750Gr3 | 934.55 | 934.36 | 767.05 | 1377.23 | 932.39 | 936.76 | 774.94 | 1359.10
ER605 v2的单向TCP性能和竞品基本一致，双向TCP性能高于竞品至少700Mbps;
ER605 v2的单双向UDP报文转发性能均优于竞品，且小包下ER605 v2的包转发速率比竞品高近750Mbps，优势显著;
ER605 v2的PPTP/L2TP 性能优于竞品，SHA1加密方式下的IPSec性能与竞品相当，但比竞品多了IPSec VPN SHA2加密算法及OpenVPN
【TCP性能】
【UDP性能】
ER605 v2 vs MikroTik hEX
机型 | 上行（Mbps） |  |  | 下行(Mbps) |  |  | 双向(Mbps) |  | 
 | 66 | 1518 | Imix | 66 | 1518 | Imix | 66 | 1518 | Imix
ER605 v2 | 954.4 | 997.5 | 989.1 | 954.5 | 997.5 | 989.7 | 1130 | 1965 | 1824.4
ER605 v1 | 949.6 | 997.5 | 989.7 | 950.1 | 997.4 | 989.5 | 1062.4 | 1920 | 1764
RB750Gr3 | 196 | 997.4 | 855 | 161 | 997 | 655 | 248 | 1000 | 970
VPN性能数据 (Mbps) |  |  |  | 
VPN类型 | 加密算法 | ER605v2 | ER605v1 | RB750G
IPSEC | esp-md5-des | 132.3 | 34.7 | 49.8
 | esp-md5-3des | 142.8 | 18.7 | 238
 | esp-md5-aes128 | 192.7 | 41.1 | 234.9
 | esp-md5-aes192 | 193.5 | 37.6 | 233.3
 | esp-md5-aes256 | 171.3 | 36.9 | 233.6
 | esp-sha1-des | 250.1 | 32 | 44.8
 | esp-sha1-3des | 234.8 | 20.1 | 235.8
 | esp-sha1-aes128 | 233.9 | 40.6 | 234
 | esp-sha1-aes192 | 240.8 | 39.8 | 237.13
 | esp-sha1-aes256 | 224.9 | 34.9 | 232.1
 | esp-sha2-des | 233.4 | N/A | N/A
 | esp-sha2-3des | 251.3 | N/A | N/A
 | esp-sha2-aes128 | 241.2 | N/A | N/A
 | esp-sha2-aes192 | 252.9 | N/A | N/A
 | esp-sha2-aes256 | 248 | N/A | N/A
L2TP | Unencrypted | 864.6 | 684.3 | 317
 | Encrypted | 47.1 | 17 | 127.4
PPTP | Unencrypted | 703.2 | 783.9 | 327.4
 | Encrypted | 76.6 | 63.2 | 115.2
OpenVPN | / | 21.7 | 22.5 | N/A

## Slide 38
ER7206 v1 vs UBNT USG
对比项 |  | TP-Link ER7206 ( ER7206) | UBNT USG
优势项 | CPU | 2 Cores @1GHz | 2 Cores @500MHz
 | 物理接口 | 1* SFP； 5* RJ45 GE; | 3* RJ45 GE
 | 多WAN口和Load balance | √ | ×
 | Routing | Static Routing Policy Routing Link Backup | Static Routing
 | UDP性能 | ER7206的小包报文转发性能显著优于竞品USG | 
 | PPTP VPN | ER7206的PPTP VPN Throughput为115.63Mbps（加密），而USG的PPTP隧道无法建立稳定连接 | 
 | L2TP VPN | L2TP Server L2TP Client | L2TP Server
 | IPSec VPN | ER7206的IPSec VPN Throughput比USG高近220Mbps | 
 | OpenVPN | OpenVPN Server OpenVPN Client | OpenVPN Client
 | 连接数 | ER7206的新建连接和最大连接数均显著优于USG | 
 | NAT ALG | √ | ×
 | 壳体 | 226*131.2*35 mm | 135*135*28.3 mm
劣势项 | Deep Packet Inspection (DPI) | × | √
 | Intrusion Prevention System (IPS) | × | √
 | IPv6 | Developing | √
 | DHCP Relay | Developing | √
新增了SFP口、OpenVPN、Multi-net DHCP等常用功能，且支持SDN，可满足中小企业网场景；
用于替代 ER6120、 ER6020，但壳体尺寸改成了桌面型，不可上机架；
NAT、VPN、Session数等关键性能优于UBNT竞品USG；

## Slide 39
连接数 | ER7206 ( ER7206) | USG
最大并发连接数 | 150,000 | 60,000
新建连接速率 | 5,500 | 400
Chart: UDP报文转发率 / Mbps
| 66 | 1518 | Imix | 66 | 1518 | Imix | 66 | 1518 | Imix | 上行 | 下行 | 双向
ER7206 (TL-ER7206) | 334.998 | 997.421 | 980.285 | 336.001 | 996.98 | 970.445 | 336.001 | 1992 | 1446.017
USG | 188.213 | 999.995 | 822.519 | 190.001 | 999.995 | 822.342 | 313.999 | 1999.978 | 1486.285
Chart: VPN性能 / Mbps
| esp-md5-aes256 | esp-sha1-aes256 | Encrypted | Encrypted | L2TP | PPTP
ER7206 (TL-ER7206) | 278.879 | 291.568 | 202.286 | 115.63
USG | 47.269 | 45.169 | 0 | 0
实际网络中实测带机量700+，日均流量超过2Tbps;
ER7206 v1 vs UBNT USG

## Slide 40: ER707-M2竞品对比
差异项 | TP-Link ER707-M2 | DrayTek Vigor2962
Ports | 1× 2.5G RJ45 WAN Port, 1× 2.5G RJ45 WAN/LAN Port, 1× Gigabit SFP WAN/LAN Port, 4× Gigabit RJ45 WAN/LAN Ports | 1× 2.5G RJ45 WAN/LAN 1× Gigabit SFP/RJ45 Combo WAN/LAN 2× Gigabit RJ45 WAN/LAN 2× Gigabit RJ45 LAN
USB Port | 1× USB 2.0（支持USB存储和USB LTE Dongle） | 1× USB 3.0 (支持存储和USB温度监控) 1× USB 2.0
WAN Port Number | up to 6 simultaneous WANs | up to 2 simultaneous WANs
Power supply | 12V / 1.5A Adapter | 110-220V AC
Surge | 4 kV | No
Dimension | 226 × 131 × 35 mm | 273 mm x 171 mm x 45 mm
Mount | Desktop / Wall-mount | Rack-mount
VPN | IPSec、L2TP、PPTP、GRE*、OPenVPN、SSL VPN（Wireguard正在开发，后续软件升级支持） | IPSec、L2TP、PPTP、GRE、Wireguard、OPenVPN、SSL VPN
LTE Feature | √（需额外购买USB LTE Dongle） | ×
Routing | Static Route、Policy Route（RIP和OSPF正在开发，后续软件升级支持） | Static Route、Policy Route、RIP、OSPF、BGP
NAT | DMZ、Port Triggering、ALG、One-to-One、Virtual Servers | DMZ、Port Triggering、ALG、Port Redirection
Bandwidth Management | Session Limit、Bandwidth Limit、Load Balance（QoS正在开发中，后续软件升级支持） | Session Limit、Bandwidth Limit、QoS、Load Balance
Security | Anti ARP Spoofing、Attack Defense、Mac Filtering、Access Control、URL Filtering、Web Filtering（Content Filtering正在去找第三方合作商，DNS Filtering已经规划后续软件迭代支持） | Attack Defense、Access Control、Content Filtering、URL Filtering、Web Filtering、DNS Filtering

## Slide 41: ER707-M2竞品对比
机型 | TCP——Static IP拨号（Mbps） |  |  | TCP——PPPoE拨号（Mbps） |  | 
 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向
TP-Link ER707-M2 | 2364.449 | 2343.275 | 4426.619 | 2350.929 | 2125.83 | 3539.274
DrayTek Vigor2962 | 2314.221 | 2283.657 | 3562.187 | 2112.211 | 2107.029 | 3050.496
ER707-M2的CPU支持硬件加速引擎，因而其在各种拨号方式下的TCP报文转发性能均显著优于DrayTek Vigor2962；
ER707-M2在不同包长下的UDP报文转发速率全面显著优于DrayTek Vigor2962。在66字节小包环境下，其UDP报文单向转发速率为DrayTek Vigor2962的4倍；
ER707-M2的不同种类、不同加密算法下的VPN性能相较于DrayTek Vigor2962各有优劣；
ER707-M2的新建连接数和最大连接数均显著优于DrayTek Vigor2962；
机型 | 66字节（Mbps） |  |  | 1518字节（Mbps） |  |  | Imix包长（Mbps） |  | 
 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向
TP-Link ER707-M2 | 1832.69 | 1741.84 | 3573.30 | 2461.18 | 2457.32 | 4982.47 | 2333.29 | 2292.48 | 4631.46
DrayTek Vigor2962 | 437.63 | 451.83 | 441.62 | 2437.33 | 2461.17 | 3700.22 | 1882.99 | 1814.22 | 1835.47
VPN类型 | 加密算法 | TCP性能Mbps |  | 
 |  | ER7206 v1 | ER707-M2 | DrayTek Vigor2962
IPSec | esp-sha1-aes128 | 293.381 | 772.087 | 1355.623
 | esp-sha1-aes192 | 293.879 | 773.42 | 1339.849
 | esp-sha1-aes256 | 291.568 | 754.646 | 1336.729
L2TP | Encrypted | 202.286 | 346.427 | 75.911
PPTP | Encrypted | 115.63 | 228.73 | 275.239
OpenVPN | UDP | / | 141.666 | 55.349
 | TCP | / | 154.913 | 9.185
SSL VPN | / | / | 142.995 | 491.346
GRE* | Encrypted | / | 376.243 | 不支持该功能
机型 | 新建连接数 (Session/s) | 最大连接数 (Session)
TP-Link ER707-M2 | 4,200 | 500,000
DrayTek Vigor2962 | 500 | 13,000
【TCP性能】
【UDP性能】
【VPN性能】
【连接数性能】

## Slide 42: ER8411竞品对比
差异项 | TP-Link ER8411 | UBNT UDM-Pro | MikroTik CCR1009-7G-1C-1S+ | MikroTik CCR2004-1G-12S+2XS
CPU | Quad-Core Cortex-A72 @2.2GHz | Quad- Core Cortex-A57 @1.7 GHz | 9-Core TILE @1.2GHz | Quad- Core Cortex-A57 @1.7 GHz
存储 | 4MB Nor Flash + 256MB NAND Flash + 4GB DDR4 | 16GB eMMC Flash + 4GB DDR4 | 128 MB NAND Flash + 2GB | 128 MB NAND Flash + 4GB
端口 | 1* 10G SFP+ WAN, 1* 10G SFP+ WAN/LAN 1* Gigabit SFP WAN/LAN 8* Gigabit RJ45 WAN/LAN | 1* 10G SFP+ WAN, 1* 10G SFP+ LAN, 1* Gigabit RJ45 WAN 8* Gigabit RJ45 LAN | 1* 10G SFP+ 1* SFP/RJ45 Combo 7* Gigabit RJ45 (均为WAN/LAN口) | 2* 25G SFP28 12* 10G SFP+ 1* Gigabit RJ45 (均为WAN/LAN口)
Console | 1* RJ45 | × | 1* RS232 | 1* RJ45
外设储存 | 2* USB 3.0（1个支持插入USB LTE Dongle） | 1个硬盘槽 | 1* Micro-USB（用于供电） | ×
Power | 2* AC (Backup) | 1* AC + 1* DC RPS | 2* AC (Backup) | 2* AC (Backup)
主板温度监控 | √ | × | √ | √
FAN | 2 | 1 | 2 | 2
内置Controller | × | √ | × | ×
SSL VPN | √ | × | × | ×
LTE Feature | √（需额外购买USB LTE Dongle） | × | × | ×
动态路由 | × | × | √（RIP, OSP, BGP） | √（RIP, OSP, BGP）
组播路由 | × | × | √ | √
VRRP | × | × | √ | √
DPI | × | √ | × | ×
IPS | × | √ | × | ×

## Slide 43: ER8411竞品对比
机型 | TCP——Static IP拨号（Mbps） |  |  | TCP——PPPoE拨号（Mbps） |  | 
 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向
TP-Link ER8411 | 9445.82 | 9449.26 | 18669.96 | 9413.96 | 9102.01 | 11310.41
UBNT UDM-Pro | 7875.15 | 7764.76 | 6209.24 | 1570.72 | 852.53 | 1058.97
MikroTik CCR1009-7G-1C-1S+ | 只有一个万兆口，此项无法测试 |  |  | 只有一个万兆口，此项无法测试 |  | 
MikroTik CCR2004-1G-12S+2XS | 8177.64 | 9045.38 | 8294.95 | 3782.18 | 3771.14 | 3702.12
ER8411开发了多种专业的加速引擎，因而其在各种拨号方式下的TCP报文转发性能均显著优于竞品。
ER8411在不同包长下的UDP报文转发速率全面显著优于UDM-Pro；
ER8411的SSL VPN和IPSec VPN功能和性能优于UDM-Pro和MikroTik router的相应竞品；
机型 | 64字节（Mbps） |  |  | 1518字节（Mbps） |  |  | Imix包长（Mbps） |  | 
 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向 | 上行 | 下行 | 双向
TP-Link ER8411 | 1080 | 1030 | 1720 | 9970 | 9970 | 19260 | 5320 | 4630 | 7500
UBNT UDM-Pro | 75 | 75 | 75 | 1300 | 1300 | 1270 | 320 | 320 | 320
VPN性能数据 (TCP报文 Mbps) |  |  |  |  | 
VPN类型 | 加密算法 | ER8411v1 | UDM-Pro | CCR1009-7G-1C-1S+ | CCR2004-1G-12S+2XS
SSLVPN |  | 1511.094 | 不支持此功能 | 不支持此功能 | 不支持此功能
OpenVPN |  | 1665.649 | 仅支持OpenVPN Server | 暂未成功建立隧道 | 暂未成功建立隧道
IPSEC | esp-md5-3des | 1621.67 | 126.836 | 662.557 | 732.429
 | esp-md5-aes256 | 2081.717 | 321.134 | 660.521 | 1530.357
 | esp-sha1-3des | 1698.74 | 129.694 | 665.442 | 728.245
 | esp-sha1-aes256 | 2140.451 | 298.253 | 661.042 | 1672.768
 | esp-sha2-3des | 1620.444 | 134.846 | 不支持此种加密 | 不支持此种加密
 | esp-sha2-aes256 | 2080.197 | 259.958 | 不支持此种加密 | 不支持此种加密
L2TP | Encrypted LAN-to-LAN | 1888.295 | 仅支持L2TP Server | 不支持此功能 | 不支持此功能
 | Encrypted Client-to-LAN | 2274.743 |  | 311.911 | 785.019
PPTP | Encrypted LAN-to-LAN | 189.912 | 不支持此功能 | 不支持此功能 | 不支持此功能
 | Encrypted Client-to-LAN | 170.049 |  | 439.139 | 831.746
【TCP性能】
【UDP性能】
【VPN性能】